ENGR/ECE 212

4 and 7 April, 2003

### Squaring a number

Input n-bit number representing k

Output 2n-bit number representing k2

### A purely combinational solution?

Start with some C++

### Generate some espresso input

.i 8

.o 16

.p 256

00000000 0000000000000000

00000001 0000000000000001

…………

11111110 1111110000000100

11111111 1111111000000001

.e

and some espresso output

.i 8

.o 16

.p 187

00010011 0000000101100000

01001111 0000100000000000

…………

----01-1 0000000000010000

111----- 1100000000000000

------10 0000000000000100

-------1 0000000000000001

.e

compute the gate delays and number of transistors

for 12-bit input

217873 bytes of espresso output

3026 AND-gates

average ~10 inputs

23 OR-gates

bit 1 is always 0

number of inputs range from 726 to 1

#### Try another combinational approach

The "grade school" algorithm in an array of gates

Again, compute delays and transistors

~ n * 5 delays

~ n2 * 25 transistors

Make the last approach sequential

n cycles of addition, shift, and store

MSI components needed (maximal?)

two n-bit registers

one 2n-bit register

one 2n-bit shifter

one 2n-bit adder

But you really only add n bits

Improved sequential approach

#### Could multiply by more than one bit in a cycle

### Think about multiplying in octal or hexadecimal

#### Block multiplication – divide and conquer

Squaring M7 M6 M5 M4 M3 M2 M1 M0

|  |  | M3 M2 M1 M0 * M3 M2 M1 M0 |
| --- | --- | --- |
|  | M7 M6 M5 M4 * M3 M2 M1 M0 |  |
|  | M3 M2 M1 M0 * M7 M6 M5 M4 |  |
| M7 M6 M5 M4 * M7 M6 M5 M4 |  |  |

Multiplication with Fast Discrete Fourier Transform

Schonhage-Strassen Algorithm

##### Save for multiplying 10,000 bit numbers

No advantage to using Karatsuba algorithm for squaring numbers

The State

Control Unit state (flip-flops)

Data Unit state (registers)

###### The cycle

Before the start of the cycle

Control Unit state is stable

Data Unit state is stable

Control Unit excitation inputs are available

Data Unit update values are available

External inputs should be available

Step 1 of cycle  (state setup time)

New Control Unit state is available

### New Data Unit registers are available

Step 2 of cycle (control combinational logic)

Control Unit provides “commands” to data unit

Step 3 of cycle (data unit conditions)

Data Unit conditions may be provided to control unit

Step 4 of cycle

Control Unit excitation inputs are available

Data Unit update values are available

How is the MUX input set?

Present or last value of the Shift Right register

| Control | Data |
| --- | --- |

Types of outputs

“mostly” Moore-type outputs

SELSUM is a Mealy-type output

# Text boxes

0

MUX

ADD

Load

Clear

Load

Shift L

Load

Shift R

Select which?