# Exercise 1: Ohm’s Law

Begin by reading the material on measuring voltage prepared by Prof E. J. Mastascusa at Bucknell University.  Next create the following circuit on your breadboard:

Questions:

1.  In the circuit above, the rating of the resistor is not specified (i.e., “X Ohms”).  Place a 1 kOhm resistor in the circuit, and measure and record the voltage drop across it ____________________.

2.  Measure and record the current flowing in the circuit:_____________________.

(Be sure to reconfigure the leads of your multimeter for measuring current.)

3.  Replace the 1 kOhm resistor with a 10 kOhm resistor, and again measure and record the voltage drop across the resistor ____________________.

(Be sure to reconfigure the leads of your multimeter for measuring voltage.)

4.  Measure and record the current flowing in the new circuit:_____________________.

(Be sure to reconfigure the leads of your multimeter for measuring current.)

5.  Ohm’s law: V = I x R.  Ohm’s law states that the current flowing through a resistor is proportional to the voltage drop across the resistor and inversely proportional to its resistance.  Are your findings consistent with Ohm’s law?  Explain and show calculations.