Exercise 20: Autonomous Control

The code below is available for you to use in Project 2.  Study the code and try to understand how it works.  Install the sonar, photoresistors, IR detectors, and IR emitters (also install the speaker and LED if desired) on your boe-bot per the schematics in exercises 18 and 19.  Load the program below into the Basic Stamp Editor and modify it to match your component installations.

Be sure to incrementally test each component---establish that all components are working properly.  This can be done by including the appropriate DEBUG statements and commenting out all subroutine calls except those needed to exercise the component being tested.

' {$STAMP BS2}

' {$PBASIC 2.5}

' -----[ I/O Definitions ]-------------------------------------------------

Trigger         PIN      0                      ' sonar input

Echo            PIN      1                      ' sonar output

RMotor          PIN      14                     ' left servo motor

LMotor          PIN      15                     ' right servo motor

LLineSnsIn      PIN      12                     ' left line sensor input

RLineSnsIn      PIN       3                     ' right line sensor input

LfIrOut         PIN      13                     ' left IR LED output

LfIrIn          VAR    IN11                     ' left IR sensor input

RtIrOut         PIN       8                     ' right IR LED output

RtIrIn          VAR     IN6                     ' right IR sensor input

Speaker         PIN      4                      ' piezo speaker

StartLED        PIN      5                      ' display start delay

' -----[ Constants ]-------------------------------------------------------

Trig10          CON        5                    ' sonic trigger pulse=10uS

ToCm            CON       30                    ' sonic conversion to cm

DistThresh      CON       36                    ' distance threshold

LFwdFast        CON     1000                    ' left motor forward; fast

LFwdSlow        CON      800                    ' left motor forward; slow

LStop           CON      750                    ' left motor stop

LRevSlow        CON      700                    ' left motor reverse; slow

LRevFast        CON      500                    ' left motor reverse; fast

RFwdFast        CON      500                    ' right motor forward; fast

RFwdSlow        CON      700                    ' right motor forward; slow

RStop           CON      750                    ' right motor stop

RRevSlow        CON      800                    ' right motor reverse; slow

RRevFast        CON     1000                    ' right motor reverse; fast

' -----[ Variables ]-------------------------------------------------------

Samples	      VAR     Byte                    ' # of samples for averaging

pWidth          VAR     Word                    ' sonar echo pulse width

rawDist         VAR     Word                    ' raw distance measurement

inches          VAR     Word                    ' hold distance in inches

lightLeft       VAR     Word                    ' left light sensor reading

lightRight      VAR     Word                    ' right light sensor reading

rightThresh     VAR     Word                    ' right black threshold

leftThresh      VAR     Word                    ' left black threshold

irLeft          VAR     Word                    ' left IR sensor reading

irRight         VAR     Word                    ' right IR sensor reading

temp            VAR     Byte                    ' loop index

' -----[ Initialization ]--------------------------------------------------

' Sets black threshold to 1/4 the average of the two sensor readings.

' SumoBot must be placed over black playing surface before this code runs.

Set_Threshold:                                  ' set photoresistor black

leftThresh = 0

rightThresh = 0

FOR samples = 1 TO 5  ' take five samples

GOSUB Read_Line_Sensors

leftThresh = leftThresh + lightLeft/5

rightThresh = rightThresh + lightRight/5

NEXT

leftThresh = leftThresh - leftThresh/10       ' set thresholds

rightThresh = rightThresh - rightThresh/10

GOSUB Read_Line_Sensors

'  DEBUG CR, "rightThresh "

'  DEBUG DEC rightThresh, CR

'  DEBUG CR, "lefThresh "

'  DEBUG DEC leftThresh, CR

Start_Delay:                                    ' mandatory five second delay

FOR temp = 1 TO 5

HIGH StartLED                               ' show active

PAUSE 900

LOW StartLED                                ' blink each second

FREQOUT Speaker, 100, 2500, 3000            ' beep each second

NEXT

' -----[ Main Code ]-------------------------------------------------------

Do

GOSUB Read_Line_Sensors

IF (lightLeft < leftThresh) AND (lightRight < rightThresh) THEN

GOSUB About_Face                            ' boundary dead ahead

ELSEIF (lightLeft < leftThresh) THEN

GOSUB Spin_Right                            ' boundary to the left

ELSEIF (lightRight < rightThresh) THEN

GOSUB Spin_Left                             ' boundary to the right

ELSE

PULSOUT LMotor, LFwdFast

PULSOUT RMotor, RFwdFast

GOSUB Search_For_Opponent

ENDIF

Loop

' -----[ Subroutines ]-----------------------------------------------------

Search_For_Opponent:

GOSUB Read_IR_Sensors

GOSUB Read_Sonar

IF (inches < DistThresh) THEN

GOSUB Lunge                                 ' bot dead ahead

ELSEIF (irLeft = 0) THEN

GOSUB Spin_Left                             ' bot to the left

ELSEIF (irRight = 0) THEN

GOSUB Spin_Right                            ' bot to the right

ELSE

PULSOUT LMotor, LFwdFast

PULSOUT RMotor, RFwdFast

ENDIF

RETURN

' --[ Read Sensors ]--

Read_Line_Sensors:

HIGH LLineSnsIn

HIGH RLineSnsIn

PAUSE 5

RCTIME LLineSnsIn, 1, lightLeft               ' read left sensor

RCTIME RLineSnsIn, 1, lightRight              ' read right sensor

'  DEBUG CLS

'  DEBUG "right = ", DEC lightRight, CR

'  DEBUG "left = ", DEC lightLeft, CR

RETURN

Read_Sonar:

rawDist = 0

FOR samples = 1 TO 5

PULSOUT Trigger, Trig10                     ' 10 uS trigger pulse

PULSIN Echo, 1, pWidth                      ' measure pulse

rawDist = rawDist + (pWidth / 5)

PAUSE 10

NEXT

inches = (rawDist / ToCm) */ $03EF

'  DEBUG "inches = ", DEC inches, CR

RETURN

Read_IR_Sensors:

FREQOUT LfIrOut, 1, 38500                     ' modulate left IR LED

irLeft = LfIrIn                               ' read input (1 = target)

FREQOUT RtIrOut, 1, 38500                     ' modulate right IR LED

irRight = RtIrIn

'  DEBUG "left IR = ", BIN irleft, CR

'  DEBUG "right IR = ", BIN irright, CR

RETURN

' --[Opponent Chase]--

Lunge:                                          ' locked on -- go get him!

FOR temp = 1 TO 15

PULSOUT LMotor, LFwdFast

PULSOUT RMotor, RFwdFast

PAUSE 20

NEXT

PULSOUT LMotor, LFwdFast

PULSOUT RMotor, RFwdFast

RETURN

Follow_Right:                                   ' spin right, fast

PULSOUT LMotor, LFwdFast

PULSOUT RMotor, RRevSlow

RETURN

Follow_Left:                                    ' spin left, fast

PULSOUT LMotor, LRevSlow

PULSOUT RMotor, RFwdFast

RETURN

' --[ Border Avoidance ]--

Spin_Left:                                      ' right sensor was active

FOR temp = 1 TO 20

PULSOUT LMotor, LRevFast

PULSOUT RMotor, RFwdFast

PAUSE 20

NEXT

PULSOUT LMotor, LFwdFast

PULSOUT RMotor, RFwdFast

RETURN

Spin_Right:                                     ' left sensor was active

FOR temp = 1 TO 20

PULSOUT LMotor, LFwdFast

PULSOUT RMotor, RRevFast

PAUSE 20

NEXT

PULSOUT LMotor, LFwdFast

PULSOUT RMotor, RFwdFast

RETURN

About_Face:                                     ' both sensors on Shikiri line

FOR temp = 1 TO 10                            ' back up from edge

PULSOUT LMotor, LRevFast

PULSOUT RMotor, RRevFast

PAUSE 20

NEXT

FOR temp = 1 TO 30                            ' turn around

PULSOUT LMotor, LFwdFast

PULSOUT RMotor, RRevFast

PAUSE 20

NEXT

PULSOUT LMotor, LFwdFast

PULSOUT RMotor, RFwdFast

RETURN

1.  Describe the modifications that you made to the program above in order to get it to run on your bot.