# Extra Credit Exercise: A nightlight

Create the following “nightlight” circuit on your boe-bot breadboard:

Questions:

1.  A photoresistor is a light sensitive resistor.  When it’s dark, the photoresistor’s resistance is large; when it’s light, the photoresistor’s resistance is low.  Measure and record the photoresistor’s resistance and the current flow through it in both ambient light and in the dark.  Cover the top of the photoresistor to simulate “dark”.

Dark						Ambient Light

Resistance of photoresistor:_________	Resistance of photoresistor:__________

Current through photoresistor: ________ 	Current through photoresistor: ________

2.  Using the measured values above and Kirchoff’s law and Ohm’s law, calculate the current passing through the LED and the voltage drop across the LED in both ambient light and dark.  Show your work below.

LED in Ambient Light:				LED in Dark:

Current:_______________________		Current:_________________________

Voltage:_______________________		Voltage:_________________________

3.  Verify your calculations with measurements; i.e., measure and record the voltage and current calculated above.

LED in Ambient Light:				LED in Dark:

Current:_______________________		Current:_________________________

Voltage:_______________________		Voltage:_________________________

4.  Is the performance of the nightlight consistent with what you know about LEDs?   Explain.

5. Try modifying the circuit to improve the performance of the “nightlight.”  If you are able to create a better nightlight, draw the circuit for your improved nightlight below.

(Be sure to include a resistor (>=470 Ohm) between the power sources and the LED.)