Exercise 20: IR and QTIs

Much of the material in this exercise is taken from Robotics with the Boe-Bot by Andy Lindsay.  While you are not required to read this material, it is recommended.

You can use your QTIs (or photoresistors) to detect the presence of the white boundary ring on the sumobot playing field such as shown below---let’s try to do that.

Step 1: Implement the schematic below using your QTIs.  In this configuration, the QTIs can be used to determine relative light levels.  You must mount the QTIs on the bottom of your Boe-Bot close to the floor.  The infrared diode behind its clear window must be facing the floor.

Step 2: Load the code below on your Boe-Bot.

' {$STAMP BS2}

' {$PBASIC 2.5}

' -----[ Variables ]-----------------------------------------------

timeLeft VAR Word

timeRight VAR Word

' -----[ Main Routine ]--------------------------------------------

DO

HIGH 3 	' activate Left QTI sensor

HIGH 2

PAUSE 1

RCTIME 2,1,timeLeft

LOW 3      ‘ deactivate sensor

DEBUG “leftTime = “, DEC timeLeft, CR

HIGH 7 	' activate right QTI sensor

HIGH 6

PAUSE 1

RCTIME 6,1,timeRight

LOW 7      ‘ deactivate sensor

DEBUG “rightTime = “, DEC timeRight, CR

PAUSE 50

LOOP

Step 3: Test your sensors on the sumobot battle field.  Record the average RC time measurements for both the left and right sensors below.

Average RC-time for left sensor on black surface: _______________________

Average RC-time for left sensor on white surface: _______________________

Average RC-time for right sensor on black surface: ______________________

Average RC-time for right sensor on white surface: ______________________

Step 3: Study the following program and answer the questions below.  You could also run the program on your boe-bot.  If you do run the program, be sure to change the constants to match the RC-time readings that you made above.

' {$STAMP BS2}

' {$PBASIC 2.5}

' -----[ Constants ]-----------------------------------------------

LeftDark CON 108

RightDark CON 114

LeftWhite CON 20

RightWhite CON 22

' Average light reading

LeftThreshold CON LeftWhite + LeftDark / 2

RightThreshold CON RightWhite + RightDark / 2

' -----[ Variables ]-----------------------------------------------

timeLeft VAR Word

timeRight VAR Word

' -----[ Main Routine ]--------------------------------------------

DO

GOSUB Test_Light

GOSUB Navigate

LOOP

' -----[ Subroutine - Test_Photoresistors ]------------------------

Test_Light:

HIGH 3 	' activate Left QTI sensor

HIGH 2

PAUSE 1

RCTIME 2,1,timeLeft

LOW 3      ‘ deactivate sensor

HIGH 7 	' activate right QTI sensor

HIGH 6

PAUSE 1

RCTIME 6,1,timeRight

LOW 7      ‘ deactivate sensor

RETURN

' -----[ Subroutine - Navigate ]-----------------------------------

Navigate:

IF (timeLeft < LeftThreshold) AND (timeRight < RightThreshold) THEN

PULSOUT 13, 650

PULSOUT 12, 850

ELSEIF (timeLeft < LeftThreshold) THEN

PULSOUT 13, 800

PULSOUT 12, 600

ELSEIF (timeRight < RightThreshold) THEN

PULSOUT 13, 600

PULSOUT 12, 800

ELSE

PULSOUT 13, 850

PULSOUT 12, 650

ENDIF

PAUSE 20

RETURN

1.  What is the purpose of this program?

Now, implement the IR emitter and detector configuration depicted below on your boebot breadboard.

Answer the questions below using the following program.

'{$STAMP BS2}

'{$PBASIC 2.5}

'=======================

'IR Emitter and Detector

'=======================

irDetectLeft	VAR	Bit

irDetectRight	VAR	Bit

DO

FREQOUT 1, 1, 38500

irDetectRight = IN0

FREQOUT 7, 1, 38500

irDetectLeft = IN8

DEBUG “irDetectLeft = “, BIN1  irDetectLeft, CR

DEBUG “irDetectRight = “, BIN1  irDetectRight, CR

PAUSE 50

LOOP

2.  What is the maximum distance at which an object can be detected? ________________________

3.  Complete the picture below by indicating the largest angle on either side at which an object 1 ft away can be detected.

4.  Your IR emitter and detector can also be used to detect the presence of the white boundary ring on the sumobot playing field.  This is because a white surface will reflect the IR signal (allowing it to return to the detector) and a black surface will adsorb the signal.  Reorientate your IR emitter and detector to point to the ground, and, using the program above, determine if you are able to detect the white boundary ring.

Could you detect the boundary ring using IR?  __________________________

# Text boxes

boebot

angle

P3

Right Side

P2

P6

P7

Left Side