## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 1
David Money Harris and Sarah L. Harris

## Slide 2
Background
The Game Plan
The Art of Managing Complexity
The Digital Abstraction
Number Systems
Logic Gates
Logic Levels
CMOS Transistors
Power Consumption
Chapter 1 :: Topics

## Slide 3
Microprocessors have revolutionized our world
  Cell phones, Internet, rapid advances in medicine, etc.
The semiconductor industry has grown from $21 billion in 1985 to $300 billion in 2011
Background

## Slide 4
Purpose of course:
  Understand what’s under the hood of a computer
  Learn the principles of digital design
  Learn to systematically debug increasingly complex designs
  Design and build a microprocessor
The Game Plan

## Slide 5
Abstraction
Discipline
The Three –y’s
  Hierarchy
  Modularity
  Regularity
The Art of Managing Complexity

## Slide 6
Hiding details when they aren’t important
Abstraction

## Slide 7
Intentionally restrict design choices
Example: Digital discipline
  Discrete voltages instead of continuous
  Simpler to design than analog circuits – can build more sophisticated systems
  Digital systems replacing analog predecessors:
    i.e., digital cameras, digital television, cell phones, CDs
Discipline

## Slide 8
Hierarchy
Modularity
Regularity
The Three -y’s

## Slide 9
Hierarchy
  A system divided into modules and submodules
Modularity
  Having well-defined functions and interfaces
Regularity
  Encouraging uniformity, so modules can be easily reused
The Three -y’s

## Slide 10
Hierarchy
  Three main modules: lock, stock, and barrel
  Submodules of lock: hammer, flint, frizzen, etc.
Example: The Flintlock Rifle

## Slide 11
Modularity
  Function of stock: mount barrel and lock
  Interface of stock: length and location of mounting pins
Regularity
  Interchangeable parts
Example: The Flintlock Rifle

## Slide 12
Most physical variables are continuous
  Voltage on a wire
  Frequency of an oscillation
  Position of a mass
Digital abstraction considers discrete subset of values
The Digital Abstraction

## Slide 13
Designed by Charles Babbage from 1834 – 1871
Considered to be the first digital computer
Built from mechanical gears, where each gear represented a discrete value (0-9)
Babbage died before it was finished
The Analytical Engine

## Slide 14
Two discrete values:
  1’s and 0’s
  1, TRUE, HIGH
  0, FALSE, LOW
1 and 0: voltage levels, rotating gears, fluid levels, etc.
Digital circuits use voltage levels to represent 1 and 0
Bit: Binary digit
Digital Discipline: Binary Values

## Slide 15
Born to working class parents
Taught himself mathematics and joined the faculty of Queen’s College in Ireland
Wrote An Investigation of the Laws of Thought (1854)
Introduced binary variables
Introduced the three fundamental logic operations: AND, OR, and NOT
George Boole, 1815-1864

## Slide 16
Decimal numbers
Binary numbers
Number Systems

## Slide 17
Decimal numbers
Binary numbers
Number Systems

## Slide 18
20 =
21 =
22 =
23 =
24 =
25 =
26 =
27 =
28 =
29 =
210 =
211 =
212 =
213 =
214 =
215 =
Powers of Two

## Slide 19
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
Handy to memorize up to 29
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
Powers of Two

## Slide 20
Decimal to binary conversion:
  Convert 100112 to decimal
Decimal to binary conversion:
  Convert 4710 to binary
Number Conversion

## Slide 21
Decimal to binary conversion:
  Convert 100112 to decimal
  16×1 + 8×0 + 4×0 + 2×1 + 1×1 = 1910
Decimal to binary conversion:
  Convert 4710 to binary
  32×1 + 16×0 + 8×1 + 4×1 + 2×1 + 1×1 = 1011112
Number Conversion

## Slide 22
N-digit decimal number
  How many values?
  Range?
  Example: 3-digit decimal number:
N-bit binary number
  How many values?
  Range:
  Example: 3-digit binary number:
Binary Values and Range

## Slide 23
N-digit decimal number
  How many values? 10N
  Range? [0, 10N - 1]
  Example: 3-digit decimal number:
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values? 2N
  Range: [0, 2N - 1]
  Example: 3-digit binary number:
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]
Binary Values and Range

## Slide 24
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 
1 | 1 | 
2 | 2 | 
3 | 3 | 
4 | 4 | 
5 | 5 | 
6 | 6 | 
7 | 7 | 
8 | 8 | 
9 | 9 | 
A | 10 | 
B | 11 | 
C | 12 | 
D | 13 | 
E | 14 | 
F | 15 | 
Hexadecimal Numbers

## Slide 25
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111
Hexadecimal Numbers

## Slide 26
Base 16
Shorthand for binary
Hexadecimal Numbers

## Slide 27
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
Hexadecimal to decimal conversion:
  Convert 0x4AF to decimal
Hexadecimal to Binary Conversion

## Slide 28
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
  0100 1010 11112
Hexadecimal to decimal conversion:
  Convert 4AF16 to decimal
  162×4 + 161×10 + 160×15 = 119910
Hexadecimal to Binary Conversion

## Slide 29
Bits
Bytes & Nibbles
Bytes
Bits, Bytes, Nibbles…

## Slide 30
210 = 1 kilo ≈ 1000 (1024)
220 = 1 mega ≈ 1 million (1,048,576)
230 = 1 giga ≈ 1 billion (1,073,741,824)
Large Powers of Two

## Slide 31
What is the value of 224?
How many values can a 32-bit variable represent?
Estimating Powers of Two

## Slide 32
What is the value of 224?
24 × 220 ≈ 16 million
How many values can a 32-bit variable represent?
22 × 230 ≈ 4 billion
Estimating Powers of Two

## Slide 33
Decimal
Binary
Addition

## Slide 34
Decimal
Binary
Addition

## Slide 35
Add the following 4-bit binary numbers
Add the following 4-bit binary numbers
Binary Addition Examples

## Slide 36
Add the following 4-bit binary numbers
Add the following 4-bit binary numbers
Overflow!
Binary Addition Examples

## Slide 37
Digital systems operate on a fixed number of bits
Overflow: when result is too big to fit in the available number of bits
See previous example of 11 + 6
Overflow

## Slide 38
Sign/Magnitude Numbers
Two’s Complement Numbers
Signed Binary Numbers

## Slide 39
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 =
- 6 =
Range of an N-bit sign/magnitude number:
Sign/Magnitude Numbers

## Slide 40
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 = 0110
- 6 = 1110
Range of an N-bit sign/magnitude number:
[-(2N-1-1), 2N-1-1]
Sign/Magnitude Numbers

## Slide 41
Problems:
  Addition doesn’t work, for example -6 + 6:
1110
+ 0110
10100 (wrong!)
  Two representations of 0 (± 0):
1000
0000
Sign/Magnitude Numbers

## Slide 42
Don’t have same problems as sign/magnitude numbers:
  Addition works
  Single representation for 0
Two’s Complement Numbers

## Slide 43
Msb has value of -2N-1
Most positive 4-bit number:
Most negative 4-bit number:
The most significant bit still indicates the sign (1 = negative, 0 = positive)
Range of an N-bit two’s comp number:
Two’s Complement Numbers

## Slide 44
Msb has value of -2N-1
Most positive 4-bit number: 0111
Most negative 4-bit number: 1000
The most significant bit still indicates the sign (1 = negative, 0 = positive)
  Range of an N-bit two’s comp number:
  [-(2N-1), 2N-1-1]
Two’s Complement Numbers

## Slide 45
Flip the sign of a two’s complement number
Method:
    Invert the bits
    Add 1
Example: Flip the sign of 310 = 00112
“Taking the Two’s Complement”

## Slide 46
Flip the sign of a two’s complement number
Method:
    Invert the bits
    Add 1
Example: Flip the sign of 310 = 00112
    1100
    + 1
    1101 = -310
“Taking the Two’s Complement”

## Slide 47
Take the two’s complement of 610 = 01102
What is the decimal value of 10012?
Two’s Complement Examples

## Slide 48
Take the two’s complement of 610 = 01102
    1001
    + 1
    10102 = -610
What is the decimal value of the two’s complement number 10012?
    0110
    + 1
    01112 = 710, so 10012 = -710
Two’s Complement Examples

## Slide 49
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Two’s Complement Addition

## Slide 50
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Two’s Complement Addition

## Slide 51
Extend number from N to M bits (M > N) :
  Sign-extension
  Zero-extension
Increasing Bit Width

## Slide 52
Sign bit copied to msb’s
Number value is same
Example 1:
  4-bit representation of 3 = 0011
  8-bit sign-extended value: 00000011
Example 2:
  4-bit representation of -5 = 1011
  8-bit sign-extended value: 11111011
Sign-Extension

## Slide 53
Zeros copied to msb’s
Value changes for negative numbers
Example 1:
  4-bit value = 00112 = 310
  8-bit zero-extended value: 00000011 = 310
Example 2:
  4-bit value = 1011 = -510
  8-bit zero-extended value: 00001011 = 1110
Zero-Extension

## Slide 54
Number System | Range
Unsigned | [0, 2N-1]
Sign/Magnitude | [-(2N-1-1), 2N-1-1]
Two’s Complement | [-2N-1, 2N-1-1]
For example, 4-bit representation:
Number System Comparison

## Slide 55
Perform logic functions:
  inversion (NOT), AND, OR, NAND, NOR, etc.
Single-input:
  NOT gate, buffer
Two-input:
  AND, OR, XOR, NAND, NOR, XNOR
Multiple-input
Logic Gates

## Slide 56
Single-Input Logic Gates

## Slide 57
Single-Input Logic Gates

## Slide 58
Two-Input Logic Gates

## Slide 59
Two-Input Logic Gates

## Slide 60
More Two-Input Logic Gates

## Slide 61
More Two-Input Logic Gates

## Slide 62
Multiple-Input Logic Gates

## Slide 63
Multi-input XOR: Odd parity
Multiple-Input Logic Gates

## Slide 64
Discrete voltages represent 1 and 0
For example:
  0 = ground (GND) or 0 volts
  1 = VDD or 5 volts
What about 4.99 volts? Is that a 0 or a 1?
What about 3.2 volts?
Logic Levels

## Slide 65
Range of voltages for 1 and 0
Different ranges for inputs and outputs to allow for noise
Logic Levels

## Slide 66
What is Noise?

## Slide 67
Anything that degrades the signal
  E.g., resistance, power supply noise, coupling to neighboring wires, etc.
Example: a gate (driver) outputs 5 V but, because of resistance in a long wire, receiver gets 4.5 V
What is Noise?

## Slide 68
With logically valid inputs, every circuit element must produce logically valid outputs
Use limited ranges of voltages to represent discrete values
The Static Discipline

## Slide 69
Logic Levels

## Slide 70
NMH = VOH – VIH
NML = VIL – VOL
Noise Margins

## Slide 71
Ideal Buffer: Real Buffer:
NMH = NML = VDD/2
NMH , NML < VDD/2
DC Transfer Characteristics

## Slide 72
DC Transfer Characteristics

## Slide 73
In 1970’s and 1980’s, VDD = 5 V
VDD has dropped
  Avoid frying tiny transistors
  Save power
3.3 V, 2.5 V, 1.8 V, 1.5 V, 1.2 V, 1.0 V, …
Be careful connecting chips with different supply voltages
Chips operate because they contain magic smoke
Proof:
  if the magic smoke is let out, the chip stops working
VDD Scaling

## Slide 74
Logic Family | VDD | VIL | VIH | VOL | VOH
TTL | 5 (4.75 - 5.25) | 0.8 | 2.0 | 0.4 | 2.4
CMOS | 5 (4.5 - 6) | 1.35 | 3.15 | 0.33 | 3.84
LVTTL | 3.3 (3 - 3.6) | 0.8 | 2.0 | 0.4 | 2.4
LVCMOS | 3.3 (3 - 3.6) | 0.9 | 1.8 | 0.36 | 2.7
Logic Family Examples

## Slide 75
Logic gates built from transistors
3-ported voltage-controlled switch
  2 ports connected depending on voltage of 3rd
  d and s are connected (ON) when g is 1
Transistors

## Slide 76
Nicknamed “Mayor of Silicon Valley”
Cofounded Fairchild Semiconductor in 1957
Cofounded Intel in 1968
Co-invented the integrated circuit
Robert Noyce, 1927-1990

## Slide 77
Transistors built from silicon, a semiconductor
Pure silicon is a poor conductor (no free charges)
Doped silicon is a good conductor (free charges)
  n-type (free negative charges, electrons)
  p-type (free positive charges, holes)
Silicon

## Slide 78
Metal oxide silicon (MOS) transistors:
  Polysilicon (used to be metal) gate
  Oxide (silicon dioxide) insulator
  Doped silicon
MOS Transistors

## Slide 79
Gate = 0
OFF (no connection between source and drain)
Gate = 1
ON (channel between source and drain)
Transistors: nMOS

## Slide 80
pMOS transistor is opposite
  ON when Gate = 0
  OFF when Gate = 1
Transistors: pMOS

## Slide 81
Transistor Function

## Slide 82
nMOS: pass good 0’s, so connect source to GND
pMOS: pass good 1’s, so connect source to VDD
Transistor Function

## Slide 83
A | P1 | N1 | Y
0 |  |  | 
1 |  |  | 
CMOS Gates: NOT Gate

## Slide 84
A | P1 | N1 | Y
0 | ON | OFF | 1
1 | OFF | ON | 0
CMOS Gates: NOT Gate

## Slide 85
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 |  |  |  |  | 
0 | 1 |  |  |  |  | 
1 | 0 |  |  |  |  | 
1 | 1 |  |  |  |  | 
CMOS Gates: NAND Gate

## Slide 86
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 | ON | ON | OFF | OFF | 1
0 | 1 | ON | OFF | OFF | ON | 1
1 | 0 | OFF | ON | ON | OFF | 1
1 | 1 | OFF | OFF | ON | ON | 0
CMOS Gates: NAND Gate

## Slide 87
CMOS Gate Structure

## Slide 88
How do you build a three-input NOR gate?
NOR Gate

## Slide 89
NOR3 Gate

## Slide 90
How do you build a two-input AND gate?
Other CMOS Gates

## Slide 91
AND2 Gate

## Slide 92
nMOS pass 1’s poorly
pMOS pass 0’s poorly
Transmission gate is a better switch
  passes both 0 and 1 well
When EN = 1, the switch is ON:
  EN = 0 and A is connected to B
When EN = 0, the switch is OFF:
  A is not connected to B
Transmission Gates

## Slide 93
Replace pull-up network with weak pMOS transistor that is always on
pMOS transistor: pulls output HIGH only when nMOS network not pulling it LOW
Pseudo-nMOS Gates

## Slide 94
Pseudo-nMOS NOR4
Pseudo-nMOS Example

## Slide 95
Cofounded Intel in 1968 with Robert Noyce.
Moore’s Law: number of transistors on a computer chip doubles every year (observed in 1965)
Since 1975, transistor counts have doubled every two years.
Gordon Moore, 1929-

## Slide 96
“If the automobile had followed the same development cycle as the computer, a Rolls-Royce would today cost $100, get one million miles to the gallon, and explode once a year . . .”
– Robert Cringley
Moore’s Law

## Slide 97
Power = Energy consumed per unit time
  Dynamic power consumption
  Static power consumption
Power Consumption

## Slide 98
Power to charge transistor gate capacitances
  Energy required to charge a capacitance, C, to VDD is CVDD2
  Circuit running at frequency f: transistors switch (from 1 to 0 or vice versa) at that frequency
  Capacitor is charged f/2 times per second (discharging from 1 to 0 is free)
Dynamic power consumption:
Pdynamic = ½CVDD2f
Dynamic Power Consumption

## Slide 99
Power consumed when no gates are switching
Caused by the quiescent supply current, IDD (also called the leakage current)
Static power consumption:
Pstatic = IDDVDD
Static Power Consumption

## Slide 100
Estimate the power consumption of a wireless handheld computer
  VDD = 1.2 V
  C = 20 nF
  f = 1 GHz
  IDD = 20 mA
Power Consumption Example

## Slide 101
Estimate the power consumption of a wireless handheld computer
  VDD = 1.2 V
  C = 20 nF
  f = 1 GHz
  IDD = 20 mA
P = ½CVDD2f + IDDVDD
= ½(20 nF)(1.2 V)2(1 GHz) +
(20 mA)(1.2 V)
= (14.4 + 0.024) W ≈ 14.4 W
Power Consumption Example