## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 2
David Money Harris and Sarah L. Harris

## Slide 2
Introduction
Boolean Equations
Boolean Algebra
From Logic to Gates
Multilevel Combinational Logic
X’s and Z’s, Oh My
Karnaugh Maps
Combinational Building Blocks
Timing
Chapter 2 :: Topics

## Slide 3
A logic circuit is composed of:
Inputs
Outputs
Functional specification
Timing specification
Introduction

## Slide 4
Nodes
  Inputs: A, B, C
  Outputs: Y, Z
  Internal: n1
Circuit elements
  E1, E2, E3
  Each a circuit
Circuits

## Slide 5
Combinational Logic
  Memoryless
  Outputs determined by current values of inputs
Sequential Logic
  Has memory
  Outputs determined by previous and current values of inputs
Types of Logic Circuits

## Slide 6
Every element is combinational
Every node is either an input or connects to exactly one output
The circuit contains no cyclic paths
Example:
Rules of Combinational Composition

## Slide 7
Functional specification of outputs in terms of inputs
Example: S = F(A, B, Cin)
Cout = F(A, B, Cin)
Boolean Equations

## Slide 8
Complement: variable with a bar over it
A, B, C
Literal: variable or its complement
A, A, B, B, C, C
Implicant: product of literals
ABC, AC, BC
Minterm: product that includes all input variables
ABC, ABC, ABC
Maxterm: sum that includes all input variables
(A+B+C), (A+B+C), (A+B+C)
Some Definitions

## Slide 9
Y = F(A, B) =
All equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)
Form function by ORing minterms where the output is TRUE
Thus, a sum (OR) of products (AND terms)
Sum-of-Products (SOP) Form

## Slide 10: Sum-of-Products Form
Y = F(A, B) =
Sum-of-Products (SOP) Form
All equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)
Form function by ORing minterms where the output is TRUE
Thus, a sum (OR) of products (AND terms)

## Slide 11: Sum-of-Products Form
Y = F(A, B) = AB + AB = Σ(1, 3)
Sum-of-Products (SOP) Form
All equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)
Form function by ORing minterms where the output is TRUE
Thus, a sum (OR) of products (AND terms)

## Slide 12
Y = F(A, B) = (A + B)(A + B) = Π(0, 2)
All Boolean equations can be written in POS form
Each row has a maxterm
A maxterm is a sum (OR) of literals
Each maxterm is FALSE for that row (and only that row)
Form function by ANDing the maxterms for which the output is FALSE
Thus, a product (AND) of sums (OR terms)
Product-of-Sums (POS) Form

## Slide 13
You are going to the cafeteria for lunch
  You won’t eat lunch (E)
  If it’s not open (O) or
  If they only serve corndogs (C)
Write a truth table for determining if you will eat lunch (E).
Boolean Equations Example

## Slide 14
You are going to the cafeteria for lunch
  You won’t eat lunch (E)
  If it’s not open (O) or
  If they only serve corndogs (C)
Write a truth table for determining if you will eat lunch (E).
Boolean Equations Example

## Slide 15: SOP & POS Form
SOP – sum-of-products
POS – product-of-sums

## Slide 16
SOP – sum-of-products
POS – product-of-sums
E = (O + C)(O + C)(O + C)
= Π(0, 1, 3)
E = OC
= Σ(2)
SOP & POS Form

## Slide 17
Axioms and theorems to simplify Boolean equations
Like regular algebra, but simpler: variables have only two values (1 or 0)
Duality in axioms and theorems:
  ANDs and ORs, 0’s and 1’s interchanged
Boolean Algebra

## Slide 18
Boolean Axioms

## Slide 19
B 1 = B
B + 0 = B
T1: Identity Theorem

## Slide 20
B 1 = B
B + 0 = B
T1: Identity Theorem

## Slide 21
B 0 = 0
B + 1 = 1
T2: Null Element Theorem

## Slide 22
B 0 = 0
B + 1 = 1
T2: Null Element Theorem

## Slide 23
B B = B
B + B = B
T3: Idempotency Theorem

## Slide 24
B B = B
B + B = B
T3: Idempotency Theorem

## Slide 25
B = B
T4: Identity Theorem

## Slide 26
B = B
T4: Identity Theorem

## Slide 27
B B = 0
B + B = 1
T5: Complement Theorem

## Slide 28
B B = 0
B + B = 1
T5: Complement Theorem

## Slide 29
Boolean Theorems Summary

## Slide 30
Boolean Theorems of Several Vars
Note: T8’ differs from traditional algebra: OR (+) distributes over AND (•)
(
)

## Slide 31
Y = AB + AB
Simplifying Boolean Equations
Example 1:

## Slide 32
Y = AB + AB
= B(A + A) T8
= B(1) T5’
= B T1
Simplifying Boolean Equations
Example 1:

## Slide 33
Y = A(AB + ABC)
Example 2:
Simplifying Boolean Equations

## Slide 34
Y = A(AB + ABC)
= A(AB(1 + C)) T8
= A(AB(1)) T2’
= A(AB) T1
= (AA)B T7
= AB T3
Example 2:
Simplifying Boolean Equations

## Slide 35
Y = AB = A + B
Y = A + B = A B
DeMorgan’s Theorem

## Slide 36
Backward:
  Body changes
  Adds bubbles to inputs
Forward:
  Body changes
  Adds bubble to output
Bubble Pushing

## Slide 37
What is the Boolean expression for this circuit?
Bubble Pushing

## Slide 38
What is the Boolean expression for this circuit?
Y = AB + CD
Bubble Pushing

## Slide 39
Begin at output, then work toward inputs
Push bubbles on final output back
Draw gates in a form so bubbles cancel
Bubble Pushing Rules

## Slide 40
Bubble Pushing Example

## Slide 41
Bubble Pushing Example

## Slide 42
Bubble Pushing Example

## Slide 43
Bubble Pushing Example

## Slide 44
Two-level logic: ANDs followed by ORs
Example: Y = ABC + ABC + ABC
From Logic to Gates

## Slide 45
Inputs on the left (or top)
Outputs on right (or bottom)
Gates flow from left to right
Straight wires are best
Circuit Schematics Rules

## Slide 46
Wires always connect at a T junction
A dot where wires cross indicates a connection between the wires
Wires crossing without a dot make no connection
Circuit Schematic Rules (cont.)

## Slide 47
Example: Priority Circuit
Output asserted
corresponding to
most significant
TRUE input
Multiple-Output Circuits

## Slide 48
Example: Priority Circuit
Output asserted
corresponding to
most significant
TRUE input
Multiple-Output Circuits

## Slide 49
Priority Circuit Hardware

## Slide 50
Don’t Cares

## Slide 51
Contention: circuit tries to drive output to 1 and 0
  Actual value somewhere in between
  Could be 0, 1, or in forbidden zone
  Might change with voltage, temperature, time, noise
  Often causes excessive power dissipation
Warnings:
  Contention usually indicates a bug.
  X is used for “don’t care” and contention - look at the context to tell them apart
Contention: X

## Slide 52
Floating, high impedance, open, high Z
Floating output might be 0, 1, or somewhere in between
  A voltmeter won’t indicate whether a node is floating
Tristate Buffer
Floating: Z

## Slide 53
Floating nodes are used in tristate busses
  Many different drivers
  Exactly one is active at
  once
Tristate Busses

## Slide 54
Boolean expressions can be minimized by combining terms
K-maps minimize equations graphically
PA + PA = P
Karnaugh Maps (K-Maps)

## Slide 55
Circle 1’s in adjacent squares
In Boolean expression, include only literals whose true and complement form are not in the circle
Y = AB
K-Map

## Slide 56
3-Input K-Map

## Slide 57
Y = AB + BC
3-Input K-Map

## Slide 58
Complement: variable with a bar over it
A, B, C
Literal: variable or its complement
A, A, B, B, C, C
Implicant: product of literals
ABC, AC, BC
Prime implicant: implicant corresponding to the largest circle in a K-map
K-Map Definitions

## Slide 59
Every 1 must be circled at least once
Each circle must span a power of 2 (i.e. 1, 2, 4) squares in each direction
Each circle must be as large as possible
A circle may wrap around the edges
A “don't care” (X) is circled only if it helps minimize the equation
K-Map Rules

## Slide 60
4-Input K-Map

## Slide 61
4-Input K-Map

## Slide 62
4-Input K-Map

## Slide 63
K-Maps with Don’t Cares

## Slide 64
K-Maps with Don’t Cares

## Slide 65
K-Maps with Don’t Cares

## Slide 66
Multiplexers
Decoders
Combinational Building Blocks

## Slide 67
Selects between one of N inputs to connect to output
log2N-bit select input – control input
Example: 2:1 Mux
Multiplexer (Mux)

## Slide 68
Logic gates
  Sum-of-products form
Tristates
  For an N-input mux, use N tristates
  Turn on exactly one to select the appropriate input
Multiplexer Implementations

## Slide 69
Using the mux as a lookup table
Logic using Multiplexers

## Slide 70
Reducing the size of the mux
Logic using Multiplexers

## Slide 71
N inputs, 2N outputs
One-hot outputs: only one output HIGH at once
Decoders

## Slide 72
Decoder Implementation

## Slide 73
OR minterms
Logic Using Decoders

## Slide 74
Delay between input change and output changing
How to build fast circuits?
Timing

## Slide 75
Propagation delay: tpd = max delay from input to output
Contamination delay: tcd = min delay from input to output
Propagation & Contamination Delay

## Slide 76
Delay is caused by
  Capacitance and resistance in a circuit
  Speed of light limitation
Reasons why tpd and tcd may be different:
  Different rising and falling delays
  Multiple inputs and outputs, some of which are faster than others
  Circuits slow down when hot and speed up when cold
Propagation & Contamination Delay

## Slide 77
Critical (Long) Path: tpd = 2tpd_AND + tpd_OR
Short Path: tcd = tcd_AND
Critical (Long) & Short Paths

## Slide 78
When a single input change causes an output to change multiple times
Glitches

## Slide 79
What happens when A = 0, C = 1, B falls?
Glitch Example

## Slide 80
Glitch Example (cont.)

## Slide 81
Fixing the Glitch

## Slide 82
Glitches don’t cause problems because of synchronous design conventions (see Chapter 3)
It’s important to recognize a glitch: in simulations or on oscilloscope
Can’t get rid of all glitches – simultaneous transitions on multiple inputs can also cause glitches
Why Understand Glitches?