## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 6
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 6 :: Topics
Introduction
Assembly Language
Machine Language
Programming
Addressing Modes
Lights, Camera, Action: Compiling, Assembling, & Loading
Odds and Ends

## Slide 3
Jumping up a few levels of abstraction
Architecture: programmer’s view of computer
  Defined by instructions & operand locations
Microarchitecture: how to implement an architecture in hardware (covered in Chapter 7)
Introduction

## Slide 4
Instructions: commands in a computer’s language
  Assembly language: human-readable format of instructions
  Machine language: computer-readable format (1’s and 0’s)
MIPS architecture:
  Developed by John Hennessy and his colleagues at Stanford and in the 1980’s.
  Used in many commercial systems, including Silicon Graphics, Nintendo, and Cisco
Once you’ve learned one architecture, it’s easy to learn others
Assembly Language

## Slide 5
President of Stanford University
Professor of Electrical Engineering and Computer Science at Stanford since 1977
Coinvented the Reduced Instruction Set Computer (RISC) with David Patterson
Developed the MIPS architecture at Stanford in 1984 and cofounded MIPS Computer Systems
As of 2004, over 300 million MIPS microprocessors have been sold
John Hennessy

## Slide 6
Underlying design principles, as articulated by Hennessy and Patterson:
    Simplicity favors regularity
    Make the common case fast
    Smaller is faster
    Good design demands good compromises
Architecture Design Principles

## Slide 7
add: mnemonic indicates operation to perform
b, c: source operands (on which the operation is performed)
a: destination operand (to which the result is written)
C Code
a = b + c;
MIPS assembly code
add a, b, c
Instructions: Addition

## Slide 8
Similar to addition - only mnemonic changes
sub: mnemonic
b, c: source operands
a: destination operand
C Code
a = b - c;
MIPS assembly code
sub a, b, c
Instructions: Subtraction

## Slide 9
Simplicity favors regularity
Consistent instruction format
Same number of operands (two sources and one destination)
Easier to encode and handle in hardware
Design Principle 1

## Slide 10
More complex code is handled by multiple MIPS instructions.
C Code
a = b + c - d;
MIPS assembly code
add t, b, c # t = b + c
sub a, t, d # a = t - d
Multiple Instructions

## Slide 11
Make the common case fast
MIPS includes only simple, commonly used instructions
Hardware to decode and execute instructions can be simple, small, and fast
More complex instructions (that are less common) performed using multiple simple instructions
MIPS is a reduced instruction set computer (RISC), with a small number of simple instructions
Other architectures, such as Intel’s x86, are complex instruction set computers (CISC)
Design Principle 2

## Slide 12
Operand location: physical location in computer
  Registers
  Memory
  Constants (also called immediates)
Operands

## Slide 13
MIPS has 32 32-bit registers
Registers are faster than memory
MIPS called “32-bit architecture” because it operates on 32-bit data
Operands: Registers

## Slide 14
Smaller is Faster
MIPS includes only a small number of registers
Design Principle 3

## Slide 15
Name | Register Number | Usage
$0 | 0 | the constant value 0
$at | 1 | assembler temporary
$v0-$v1 | 2-3 | Function return values
$a0-$a3 | 4-7 | Function arguments
$t0-$t7 | 8-15 | temporaries
$s0-$s7 | 16-23 | saved variables
$t8-$t9 | 24-25 | more temporaries
$k0-$k1 | 26-27 | OS temporaries
$gp | 28 | global pointer
$sp | 29 | stack pointer
$fp | 30 | frame pointer
$ra | 31 | Function return address
MIPS Register Set

## Slide 16
Registers:
  $ before name
  Example: $0, “register zero”, “dollar zero”
Registers used for specific purposes:
    $0 always holds the constant value 0.
    the saved registers, $s0-$s7, used to hold variables
    the temporary registers, $t0 - $t9, used to hold intermediate values during a larger computation
    Discuss others later
Operands: Registers

## Slide 17
Revisit add instruction
C Code
a = b + c
MIPS assembly code
# $s0 = a, $s1 = b, $s2 = c
add $s0, $s1, $s2
Instructions with Registers

## Slide 18
Too much data to fit in only 32 registers
Store more data in memory
Memory is large, but slow
Commonly used variables kept in registers
Operands: Memory

## Slide 19
Each 32-bit data word has a unique address
Word-Addressable Memory
Note: MIPS uses byte-addressable memory, which we’ll talk about next.

## Slide 20
Memory read called load
Mnemonic: load word (lw)
Format:
lw $s0, 5($t1)
Address calculation:
  add base address ($t1) to the offset (5)
  address = ($t1 + 5)
Result:
  $s0 holds the value at address ($t1 + 5)
Any register may be used as base address
Reading Word-Addressable Memory

## Slide 21
Example: read a word of data at memory address 1 into $s3
  address = ($0 + 1) = 1
  $s3 = 0xF2F1AC07 after load
Assembly code
lw $s3, 1($0) # read memory word 1 into $s3
Reading Word-Addressable Memory

## Slide 22
Memory write are called store
Mnemonic: store word (sw)
Writing Word-Addressable Memory

## Slide 23
Example: Write (store) the value in $t4 into memory address 7
  add the base address ($0) to the offset (0x7)
  address: ($0 + 0x7) = 7
  Offset can be written in decimal (default) or hexadecimal
Assembly code
sw $t4, 0x7($0) # write the value in $t4
# to memory word 7
Writing Word-Addressable Memory

## Slide 24
Each data byte has unique address
Load/store words or single bytes: load byte (lb) and store byte (sb)
32-bit word = 4 bytes, so word address increments by 4
Byte-Addressable Memory

## Slide 25
The address of a memory word must now be multiplied by 4. For example,
  the address of memory word 2 is 2 × 4 = 8
  the address of memory word 10 is 10 × 4 = 40 (0x28)
MIPS is byte-addressed, not word-addressed
Reading Byte-Addressable Memory

## Slide 26
Example: Load a word of data at memory address 4 into $s3.
$s3 holds the value 0xF2F1AC07 after load
MIPS assembly code
lw $s3, 4($0) # read word at address 4 into $s3
Reading Byte-Addressable Memory

## Slide 27
Example: stores the value held in $t7 into memory address 0x2C (44)
MIPS assembly code
sw $t7, 44($0) # write $t7 into address 44
Writing Byte-Addressable Memory

## Slide 28
How to number bytes within a word?
Little-endian: byte numbers start at the little (least significant) end
Big-endian: byte numbers start at the big (most significant) end
Word address is the same for big- or little-endian
Big-Endian & Little-Endian Memory

## Slide 29
Jonathan Swift’s Gulliver’s Travels: the Little-Endians broke their eggs on the little end of the egg and the Big-Endians broke their eggs on the big end
It doesn’t really matter which addressing type used – except when the two systems need to share data!
Big-Endian & Little-Endian Memory

## Slide 30
Suppose $t0 initially contains 0x23456789
After following code runs on big-endian system, what value is $s0?
In a little-endian system?
sw $t0, 0($0)
lb $s0, 1($0)
Big-Endian & Little-Endian Example

## Slide 31
Suppose $t0 initially contains 0x23456789
After following code runs on big-endian system, what value is $s0?
In a little-endian system?
sw $t0, 0($0)
lb $s0, 1($0)
Big-endian: 0x00000045
Little-endian: 0x00000067
Big-Endian & Little-Endian Example

## Slide 32
Good design demands good compromises
Multiple instruction formats allow flexibility
  add, sub: use 3 register operands
  lw, sw: use 2 register operands and a constant
Number of instruction formats kept small
  to adhere to design principles 1 and 3 (simplicity favors regularity and smaller is faster).
Design Principle 4

## Slide 33
lw and sw use constants or immediates
immediately available from instruction
16-bit two’s complement number
addi: add immediate
Subtract immediate (subi) necessary?
C Code
a = a + 4;
b = a – 12;
MIPS assembly code
# $s0 = a, $s1 = b
addi $s0, $s0, 4
addi $s1, $s0, -12
Operands: Constants/Immediates

## Slide 34
Binary representation of instructions
Computers only understand 1’s and 0’s
32-bit instructions
  Simplicity favors regularity: 32-bit data & instructions
3 instruction formats:
  R-Type: register operands
  I-Type: immediate operand
  J-Type: for jumping (discuss later)
Machine Language

## Slide 35
Register-type
3 register operands:
  rs, rt: source registers
  rd: destination register
Other fields:
  op: the operation code or opcode (0 for R-type instructions)
  funct: the function
  with opcode, tells computer what operation to perform
  shamt: the shift amount for shift instructions, otherwise it’s 0
R-Type

## Slide 36
Note the order of registers in the assembly code:
add rd, rs, rt
R-Type Examples

## Slide 37
Immediate-type
3 operands:
  rs, rt: register operands
  imm: 16-bit two’s complement immediate
Other fields:
  op: the opcode
  Simplicity favors regularity: all instructions have opcode
  Operation is completely determined by opcode
I-Type

## Slide 38
Note the differing order of registers in assembly and machine codes:
addi rt, rs, imm
lw rt, imm(rs)
sw rt, imm(rs)
I-Type Examples

## Slide 39
Jump-type
26-bit address operand (addr)
Used for jump instructions (j)
Machine Language: J-Type

## Slide 40
Review: Instruction Formats

## Slide 41
32-bit instructions & data stored in memory
Sequence of instructions: only difference between two applications
To run a new program:
  No rewiring required
  Simply store new program in memory
Program Execution:
  Processor fetches (reads) instructions from memory in sequence
  Processor performs the specified operation
Power of the Stored Program

## Slide 42
The Stored Program
Program Counter (PC): keeps track of current instruction

## Slide 43
Start with opcode: tells how to parse rest
If opcode all 0’s
  R-type instruction
  Function bits tell operation
Otherwise
  opcode tells operation
Interpreting Machine Code

## Slide 44
High-level languages:
  e.g., C, Java, Python
  Written at higher level of abstraction
Common high-level software constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls
Programming

## Slide 45
Wrote the first computer program
Her program calculated the Bernoulli numbers on Charles Babbage’s Analytical Engine
She was the daughter of the poet Lord Byron
Ada Lovelace, 1815-1852

## Slide 46
and, or, xor, nor
  and: useful for masking bits
    Masking all but the least significant byte of a value:
    0xF234012F AND 0x000000FF = 0x0000002F
  or: useful for combining bit fields
    Combine 0xF2340000 with 0x000012BC:
    0xF2340000 OR 0x000012BC = 0xF23412BC
  nor: useful for inverting bits:
    A NOR $0 = NOT A
andi, ori, xori
  16-bit immediate is zero-extended (not sign-extended)
  nori not needed
Logical Instructions

## Slide 47
Logical Instructions Example 1

## Slide 48
Logical Instructions Example 1

## Slide 49
Logical Instructions Example 2

## Slide 50
Logical Instructions Example 2

## Slide 51
sll: shift left logical
  Example: sll $t0, $t1, 5 # $t0 <= $t1 << 5
srl: shift right logical
  Example: srl $t0, $t1, 5 # $t0 <= $t1 >> 5
sra: shift right arithmetic
  Example: sra $t0, $t1, 5 # $t0 <= $t1 >>> 5
Shift Instructions

## Slide 52
sllv: shift left logical variable
  Example: sllv $t0, $t1, $t2 # $t0 <= $t1 << $t2
srlv: shift right logical variable
  Example: srlv $t0, $t1, $t2 # $t0 <= $t1 >> $t2
srav: shift right arithmetic variable
  Example: srav $t0, $t1, $t2 # $t0 <= $t1 >>> $t2
Variable Shift Instructions

## Slide 53
Shift Instructions

## Slide 54
16-bit constants using addi:
32-bit constants using load upper immediate (lui) and ori:
C Code
int a = 0xFEDC8765;
MIPS assembly code
# $s0 = a
lui $s0, 0xFEDC
ori $s0, $s0, 0x8765
C Code
// int is a 32-bit signed word
int a = 0x4f3c;
MIPS assembly code
# $s0 = a
addi $s0, $0, 0x4f3c
Generating Constants

## Slide 55
Special registers: lo, hi
32 × 32 multiplication, 64 bit result
  mult $s0, $s1
  Result in {hi, lo}
32-bit division, 32-bit quotient, remainder
  div $s0, $s1
  Quotient in lo
  Remainder in hi
Moves from lo/hi special registers
  mflo $s2
  mfhi $s3
Multiplication, Division

## Slide 56
Execute instructions out of sequence
Types of branches:
  Conditional
    branch if equal (beq)
    branch if not equal (bne)
  Unconditional
    jump (j)
    jump register (jr)
    jump and link (jal)
Branching

## Slide 57
Review: The Stored Program

## Slide 58
# MIPS assembly
addi $s0, $0, 4 # $s0 = 0 + 4 = 4
addi $s1, $0, 1 # $s1 = 0 + 1 = 1
sll $s1, $s1, 2 # $s1 = 1 << 2 = 4
beq $s0, $s1, target # branch is taken
addi $s1, $s1, 1 # not executed
sub $s1, $s1, $s0 # not executed
target: # label
add $s1, $s1, $s0 # $s1 = 4 + 4 = 8
Labels indicate instruction location. They can’t be reserved words and must be followed by colon (:)
Conditional Branching (beq)

## Slide 59
# MIPS assembly
addi $s0, $0, 4 # $s0 = 0 + 4 = 4
addi $s1, $0, 1 # $s1 = 0 + 1 = 1
sll $s1, $s1, 2 # $s1 = 1 << 2 = 4
bne $s0, $s1, target # branch not taken
addi $s1, $s1, 1 # $s1 = 4 + 1 = 5
sub $s1, $s1, $s0 # $s1 = 5 – 4 = 1
target:
add $s1, $s1, $s0 # $s1 = 1 + 4 = 5
The Branch Not Taken (bne)

## Slide 60
# MIPS assembly
addi $s0, $0, 4 # $s0 = 4
addi $s1, $0, 1 # $s1 = 1
j target # jump to target
sra $s1, $s1, 2 # not executed
addi $s1, $s1, 1 # not executed
sub $s1, $s1, $s0 # not executed
target:
add $s1, $s1, $s0 # $s1 = 1 + 4 = 5
Unconditional Branching (j)

## Slide 61
# MIPS assembly
0x00002000 addi $s0, $0, 0x2010
0x00002004 jr $s0
0x00002008 addi $s1, $0, 1
0x0000200C sra $s1, $s1, 2
0x00002010 lw $s3, 44($s1)
jr is an R-type instruction.
Unconditional Branching (jr)

## Slide 62
if statements
if/else statements
while loops
for loops
High-Level Code Constructs

## Slide 63
C Code
if (i == j)
f = g + h;
f = f – i;
MIPS assembly code
# $s0 = f, $s1 = g, $s2 = h
# $s3 = i, $s4 = j
If Statement

## Slide 64
C Code
if (i == j)
f = g + h;
f = f – i;
MIPS assembly code
# $s0 = f, $s1 = g, $s2 = h
# $s3 = i, $s4 = j
bne $s3, $s4, L1
add $s0, $s1, $s2
L1: sub $s0, $s0, $s3
Assembly tests opposite case (i != j) of high-level code (i == j)
If Statement

## Slide 65
C Code
if (i == j)
f = g + h;
else
f = f – i;
MIPS assembly code
If/Else Statement

## Slide 66
C Code
if (i == j)
f = g + h;
else
f = f – i;
MIPS assembly code
# $s0 = f, $s1 = g, $s2 = h
# $s3 = i, $s4 = j
bne $s3, $s4, L1
add $s0, $s1, $s2
j done
L1: sub $s0, $s0, $s3
done:
If/Else Statement

## Slide 67
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
MIPS assembly code
Assembly tests for the opposite case (pow == 128) of the C code (pow != 128).
While Loops

## Slide 68
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
MIPS assembly code
# $s0 = pow, $s1 = x
addi $s0, $0, 1
add $s1, $0, $0
addi $t0, $0, 128
while: beq $s0, $t0, done
sll $s0, $s0, 1
addi $s1, $s1, 1
j while
done:
Assembly tests for the opposite case (pow == 128) of the C code (pow != 128).
While Loops

## Slide 69
for (initialization; condition; loop operation)
statement
initialization: executes before the loop begins
condition: is tested at the beginning of each iteration
loop operation: executes at the end of each iteration
statement: executes each time the condition is met
For Loops

## Slide 70
High-level code
// add the numbers from 0 to 9
int sum = 0;
int i;
for (i=0; i!=10; i = i+1) {
sum = sum + i;
}
MIPS assembly code
# $s0 = i, $s1 = sum
For Loops

## Slide 71
C Code
// add the numbers from 0 to 9
int sum = 0;
int i;
for (i=0; i!=10; i = i+1) {
sum = sum + i;
}
MIPS assembly code
For Loops

## Slide 72
C Code
// add the numbers from 0 to 9
int sum = 0;
int i;
for (i=0; i!=10; i = i+1) {
sum = sum + i;
}
MIPS assembly code
# $s0 = i, $s1 = sum
addi $s1, $0, 0
add $s0, $0, $0
addi $t0, $0, 10
for: beq $s0, $t0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:
For Loops

## Slide 73
C Code
// add the powers of 2 from 1
// to 100
int sum = 0;
int i;
for (i=1; i < 101; i = i*2) {
sum = sum + i;
}
MIPS assembly code
Less Than Comparison

## Slide 74
C Code
// add the powers of 2 from 1
// to 100
int sum = 0;
int i;
for (i=1; i < 101; i = i*2) {
sum = sum + i;
}
MIPS assembly code
# $s0 = i, $s1 = sum
addi $s1, $0, 0
addi $s0, $0, 1
addi $t0, $0, 101
loop: slt $t1, $s0, $t0
beq $t1, $0, done
add $s1, $s1, $s0
sll $s0, $s0, 1
j loop
done:
$t1 = 1 if i < 101
Less Than Comparison

## Slide 75
Access large amounts of similar data
Index: access each element
Size: number of elements
Arrays

## Slide 76
5-element array
Base address = 0x12348000 (address of first element, array[0])
First step in accessing an array: load base address into a register
Arrays

## Slide 77
// C Code
int array[5];
array[0] = array[0] * 2;
array[1] = array[1] * 2;
Accessing Arrays

## Slide 78
// C Code
int array[5];
array[0] = array[0] * 2;
array[1] = array[1] * 2;
# MIPS assembly code
# $s0 = array base address
lui $s0, 0x1234 # 0x1234 in upper half of $s0
ori $s0, $s0, 0x8000 # 0x8000 in lower half of $s0
lw $t1, 0($s0) # $t1 = array[0]
sll $t1, $t1, 1 # $t1 = $t1 * 2
sw $t1, 0($s0) # array[0] = $t1
lw $t1, 4($s0) # $t1 = array[1]
sll $t1, $t1, 1 # $t1 = $t1 * 2
sw $t1, 4($s0) # array[1] = $t1
Accessing Arrays

## Slide 79
// C Code
int array[1000];
int i;
for (i=0; i < 1000; i = i + 1)
array[i] = array[i] * 8;
# MIPS assembly code
# $s0 = array base address, $s1 = i
Arrays using For Loops

## Slide 80
# MIPS assembly code
# $s0 = array base address, $s1 = i
# initialization code
lui $s0, 0x23B8 # $s0 = 0x23B80000
ori $s0, $s0, 0xF000 # $s0 = 0x23B8F000
addi $s1, $0, 0 # i = 0
addi $t2, $0, 1000 # $t2 = 1000
loop:
slt $t0, $s1, $t2 # i < 1000?
beq $t0, $0, done # if not then done
sll $t0, $s1, 2 # $t0 = i * 4 (byte offset)
add $t0, $t0, $s0 # address of array[i]
lw $t1, 0($t0) # $t1 = array[i]
sll $t1, $t1, 3 # $t1 = array[i] * 8
sw $t1, 0($t0) # array[i] = array[i] * 8
addi $s1, $s1, 1 # i = i + 1
j loop # repeat
done:
Arrays Using For Loops

## Slide 81
American Standard Code for Information Interchange
Each text character has unique byte value
  For example, S = 0x53, a = 0x61, A = 0x41
  Lower-case and upper-case differ by 0x20 (32)
ASCII Code

## Slide 82
Cast of Characters

## Slide 83
Caller: calling function (in this case, main)
Callee: called function (in this case, sum)
C Code
void main()
{
int y;
y = sum(42, 7);
...
}
int sum(int a, int b)
{
return (a + b);
}
Function Calls

## Slide 84
Caller:
  passes arguments to callee
  jumps to callee
Callee:
  performs the function
  returns result to caller
  returns to point of call
  must not overwrite registers or memory needed by caller
Function Conventions

## Slide 85
Call Function: jump and link (jal)
Return from function: jump register (jr)
Arguments: $a0 - $a3
Return value: $v0
MIPS Function Conventions

## Slide 86
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
MIPS assembly code
0x00400200 main: jal simple
0x00400204 add $s0, $s1, $s2
...
0x00401020 simple: jr $ra
void means that simple doesn’t return a value
Function Calls

## Slide 87
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
MIPS assembly code
0x00400200 main: jal simple
0x00400204 add $s0, $s1, $s2
...
0x00401020 simple: jr $ra
jal: jumps to simple
$ra = PC + 4 = 0x00400204
jr $ra: jumps to address in $ra (0x00400204)
Function Calls

## Slide 88
MIPS conventions:
Argument values: $a0 - $a3
Return value: $v0
Input Arguments & Return Value

## Slide 89
C Code
int main()
{
int y;
...
y = diffofsums(2, 3, 4, 5); // 4 arguments
...
}
int diffofsums(int f, int g, int h, int i)
{
int result;
result = (f + g) - (h + i);
return result; // return value
}
Input Arguments & Return Value

## Slide 90
MIPS assembly code
# $s0 = y
main:
...
addi $a0, $0, 2 # argument 0 = 2
addi $a1, $0, 3 # argument 1 = 3
addi $a2, $0, 4 # argument 2 = 4
addi $a3, $0, 5 # argument 3 = 5
jal diffofsums # call Function
add $s0, $v0, $0 # y = returned value
...
# $s0 = result
diffofsums:
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + i
sub $s0, $t0, $t1 # result = (f + g) - (h + i)
add $v0, $s0, $0 # put return value in $v0
jr $ra # return to caller
Input Arguments & Return Value

## Slide 91
MIPS assembly code
# $s0 = result
diffofsums:
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + i
sub $s0, $t0, $t1 # result = (f + g) - (h + i)
add $v0, $s0, $0 # put return value in $v0
jr $ra # return to caller
diffofsums overwrote 3 registers: $t0, $t1, $s0
diffofsums can use stack to temporarily store registers
Input Arguments & Return Value

## Slide 92
Memory used to temporarily save variables
Like stack of dishes, last-in-first-out (LIFO) queue
Expands: uses more memory when more space needed
Contracts: uses less memory when the space is no longer needed
The Stack

## Slide 93
Grows down (from higher to lower memory addresses)
Stack pointer: $sp points to top of the stack
The Stack

## Slide 94
# MIPS assembly
# $s0 = result
diffofsums:
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + i
sub $s0, $t0, $t1 # result = (f + g) - (h + i)
add $v0, $s0, $0 # put return value in $v0
jr $ra # return to caller
Called functions must have no unintended side effects
But diffofsums overwrites 3 registers: $t0, $t1, $s0
How Functions use the Stack

## Slide 95
# $s0 = result
diffofsums:
addi $sp, $sp, -12 # make space on stack
# to store 3 registers
sw $s0, 8($sp) # save $s0 on stack
sw $t0, 4($sp) # save $t0 on stack
sw $t1, 0($sp) # save $t1 on stack
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + i
sub $s0, $t0, $t1 # result = (f + g) - (h + i)
add $v0, $s0, $0 # put return value in $v0
lw $t1, 0($sp) # restore $t1 from stack
lw $t0, 4($sp) # restore $t0 from stack
lw $s0, 8($sp) # restore $s0 from stack
addi $sp, $sp, 12 # deallocate stack space
jr $ra # return to caller
Storing Register Values on the Stack

## Slide 96
The stack during diffofsums Call

## Slide 97
Preserved Callee-Saved | Nonpreserved Caller-Saved
$s0-$s7 | $t0-$t9
$ra | $a0-$a3
$sp | $v0-$v1
stack above $sp | stack below $sp
Registers

## Slide 98
proc1:
addi $sp, $sp, -4 # make space on stack
sw $ra, 0($sp) # save $ra on stack
jal proc2
...
lw $ra, 0($sp) # restore $s0 from stack
addi $sp, $sp, 4 # deallocate stack space
jr $ra # return to caller
Multiple Function Calls

## Slide 99
# $s0 = result
diffofsums:
addi $sp, $sp, -4 # make space on stack to
# store one register
sw $s0, 0($sp) # save $s0 on stack
# no need to save $t0 or $t1
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + i
sub $s0, $t0, $t1 # result = (f + g) - (h + i)
add $v0, $s0, $0 # put return value in $v0
lw $s0, 0($sp) # restore $s0 from stack
addi $sp, $sp, 4 # deallocate stack space
jr $ra # return to caller
Storing Saved Registers on the Stack

## Slide 100
High-level code
int factorial(int n) {
if (n <= 1)
return 1;
else
return (n * factorial(n-1));
}
Recursive Function Call

## Slide 101
MIPS assembly code
Recursive Function Call

## Slide 102
MIPS assembly code
0x90 factorial: addi $sp, $sp, -8 # make room
0x94 sw $a0, 4($sp) # store $a0
0x98 sw $ra, 0($sp) # store $ra
0x9C addi $t0, $0, 2
0xA0 slt $t0, $a0, $t0 # a <= 1 ?
0xA4 beq $t0, $0, else # no: go to else
0xA8 addi $v0, $0, 1 # yes: return 1
0xAC addi $sp, $sp, 8 # restore $sp
0xB0 jr $ra # return
0xB4 else: addi $a0, $a0, -1 # n = n - 1
0xB8 jal factorial # recursive call
0xBC lw $ra, 0($sp) # restore $ra
0xC0 lw $a0, 4($sp) # restore $a0
0xC4 addi $sp, $sp, 8 # restore $sp
0xC8 mul $v0, $a0, $v0 # n * factorial(n-1)
0xCC jr $ra # return
Recursive Function Call

## Slide 103
Stack During Recursive Call

## Slide 104
Caller
  Put arguments in $a0-$a3
  Save any needed registers ($ra, maybe $t0-t9)
  jal callee
  Restore registers
  Look for result in $v0
Callee
  Save registers that might be disturbed ($s0-$s7)
  Perform function
  Put result in $v0
  Restore registers
  jr $ra
Function Call Summary

## Slide 105
How do we address the operands?
Register Only
Immediate
Base Addressing
PC-Relative
Pseudo Direct
Addressing Modes

## Slide 106
Register Only
Operands found in registers
  Example: add $s0, $t2, $t3
  Example: sub $t8, $s1, $0
Immediate
16-bit immediate used as an operand
  Example: addi $s4, $t5, -73
  Example: ori $t3, $t7, 0xFF
Addressing Modes

## Slide 107
Base Addressing
Address of operand is:
  base address + sign-extended immediate
  Example: lw $s4, 72($0)
    address = $0 + 72
  Example: sw $t2, -25($t1)
    address = $t1 - 25
Addressing Modes

## Slide 108
PC-Relative Addressing
0x10 beq $t0, $0, else
0x14 addi $v0, $0, 1
0x18 addi $sp, $sp, i
0x1C jr $ra
0x20 else: addi $a0, $a0, -1
0x24 jal factorial
Addressing Modes

## Slide 109
Pseudo-direct Addressing
0x0040005C jal sum
...
0x004000A0 sum: add $v0, $a0, $a1
Addressing Modes

## Slide 110
How to Compile & Run a Program

## Slide 111
Graduated from Yale University with a Ph.D. in mathematics
Developed first compiler
Helped develop the COBOL programming language
Highly awarded naval officer
Received World War II Victory Medal and National Defense Service Medal, among others
Grace Hopper, 1906-1992

## Slide 112
Instructions (also called text)
Data
  Global/static: allocated before program begins
  Dynamic: allocated within program
How big is memory?
  At most 232 = 4 gigabytes (4 GB)
  From address 0x00000000 to 0xFFFFFFFF
What is Stored in Memory?

## Slide 113
MIPS Memory Map

## Slide 114
int f, g, y; // global variables
int main(void)
{
f = 2;
g = 3;
y = sum(f, g);
return y;
}
int sum(int a, int b) {
return (a + b);
}
Example Program: C Code

## Slide 115
int f, g, y; // global
int main(void)
{
f = 2;
g = 3;
y = sum(f, g);
return y;
}
int sum(int a, int b) {
return (a + b);
}
.data
f:
g:
y:
.text
main:
addi $sp, $sp, -4 # stack frame
sw $ra, 0($sp) # store $ra
addi $a0, $0, 2 # $a0 = 2
sw $a0, f # f = 2
addi $a1, $0, 3 # $a1 = 3
sw $a1, g # g = 3
jal sum # call sum
sw $v0, y # y = sum()
lw $ra, 0($sp) # restore $ra
addi $sp, $sp, 4 # restore $sp
jr $ra # return to OS
sum:
add $v0, $a0, $a1 # $v0 = a + b
jr $ra # return
Example Program: MIPS Assembly

## Slide 116
Symbol | Address
Example Program: Symbol Table

## Slide 117
Symbol | Address
f | 0x10000000
g | 0x10000004
y | 0x10000008
main | 0x00400000
sum | 0x0040002C
Example Program: Symbol Table

## Slide 118
Example Program: Executable

## Slide 119
Example Program: In Memory

## Slide 120
Pseudoinstructions
Exceptions
Signed and unsigned instructions
Floating-point instructions
Odds & Ends

## Slide 121
Pseudoinstruction | MIPS Instructions
li $s0, 0x1234AA77 | lui $s0, 0x1234 ori $s0, 0xAA77
clear $t0 | add $t0, $0, $0
move $s1, $s2 | add $s2, $s1, $0
nop | sll $0, $0, 0
Pseudoinstructions

## Slide 122
Unscheduled function call to exception handler
Caused by:
  Hardware, also called an interrupt, e.g., keyboard
  Software, also called traps, e.g., undefined instruction
When exception occurs, the processor:
  Records the cause of the exception
  Jumps to exception handler (at instruction address 0x80000180)
  Returns to program
Exceptions

## Slide 123
Not part of register file
  Cause: Records cause of exception
  EPC (Exception PC): Records PC where exception occurred
EPC and Cause: part of Coprocessor 0
Move from Coprocessor 0
  mfc0 $k0, EPC
  Moves contents of EPC into $k0
Exception Registers

## Slide 124
Exception | Cause
Hardware Interrupt | 0x00000000
System Call | 0x00000020
Breakpoint / Divide by 0 | 0x00000024
Undefined Instruction | 0x00000028
Arithmetic Overflow | 0x00000030
Exception Causes

## Slide 125
Processor saves cause and exception PC in Cause and EPC
Processor jumps to exception handler (0x80000180)
Exception handler:
  Saves registers on stack
  Reads Cause register
  mfc0 $k0, Cause
  Handles exception
  Restores registers
  Returns to program
    mfc0 $k0, EPC
    jr $k0
Exception Flow

## Slide 126
Addition and subtraction
Multiplication and division
Set less than
Signed & Unsigned Instructions

## Slide 127
Signed: add, addi, sub
  Same operation as unsigned versions
  But processor takes exception on overflow
Unsigned: addu, addiu, subu
  Doesn’t take exception on overflow
  Note: addiu sign-extends the immediate
Addition & Subtraction

## Slide 128
Signed: mult, div
Unsigned: multu, divu
Multiplication & Division

## Slide 129
Signed: slt, slti
Unsigned: sltu, sltiu
Note: sltiu sign-extends the immediate before comparing it to the register
Set Less Than

## Slide 130
Signed:
  Sign-extends to create 32-bit value to load into register
  Load halfword: lh
  Load byte: lb
Unsigned:
  Zero-extends to create 32-bit value
  Load halfword unsigned: lhu
  Load byte: lbu
Loads

## Slide 131
Floating-point coprocessor (Coprocessor 1)
32 32-bit floating-point registers ($f0-$f31)
Double-precision values held in two floating point registers
  e.g., $f0 and $f1, $f2 and $f3, etc.
  Double-precision floating point registers: $f0, $f2, $f4, etc.
Floating-Point Instructions

## Slide 132
Name | Register Number | Usage
$fv0 - $fv1 | 0, 2 | return values
$ft0 - $ft3 | 4, 6, 8, 10 | temporary variables
$fa0 - $fa1 | 12, 14 | Function arguments
$ft4 - $ft8 | 16, 18 | temporary variables
$fs0 - $fs5 | 20, 22, 24, 26, 28, 30 | saved variables
Floating-Point Instructions

## Slide 133
Opcode = 17 (0100012)
Single-precision:
  cop = 16 (0100002)
  add.s, sub.s, div.s, neg.s, abs.s, etc.
Double-precision:
  cop = 17 (0100012)
  add.d, sub.d, div.d, neg.d, abs.d, etc.
3 register operands:
  fs, ft: source operands
  fd: destination operands
F-Type Instruction Format

## Slide 134
Set/clear condition flag: fpcond
  Equality: c.seq.s, c.seq.d
  Less than: c.lt.s, c.lt.d
  Less than or equal: c.le.s, c.le.d
Conditional branch
  bclf: branches if fpcond is FALSE
  bclt: branches if fpcond is TRUE
Loads and stores
  lwc1: lwc1 $ft1, 42($s1)
  swc1: swc1 $fs2, 17($sp)
Floating-Point Branches

## Slide 135
Microarchitecture – building MIPS processor in hardware
Bring colored pencils
Looking Ahead