## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 5
David Money Harris and Sarah L. Harris
Edited by J Dean Brock
For CSCI 320

## Slide 2
Chapter 5 :: Topics
Introduction
Arithmetic Circuits
Number Systems
Sequential Building Blocks
Memory Arrays
Logic Arrays

## Slide 3
Digital building blocks:
  Gates, multiplexers, decoders, registers, arithmetic circuits, counters, memory arrays, logic arrays
Building blocks demonstrate hierarchy, modularity, and regularity:
  Hierarchy of simpler components
  Well-defined interfaces and functions
  Regular structure easily extends to different sizes
Will use these building blocks in Chapter 7 to build microprocessor
Introduction

## Slide 4
1-Bit Adders
I think we did this in the lab

## Slide 5
Types of carry propagate adders (CPAs):
  Ripple-carry (slow)
  Carry-lookahead (fast)
  Prefix (faster)
Carry-lookahead and prefix adders faster for large adders but require more hardware
  Symbol
Multibit Adders (CPAs)

## Slide 6
Chain 1-bit adders together
Carry ripples through entire chain
Disadvantage: slow
Ripple-Carry Adder

## Slide 7
Compute carry out (Cout) for k-bit blocks using generate and propagate signals
Some definitions:
  Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
  Generate (Gi) and propagate (Pi) signals for each column:
    Column i will generate a carry out if Ai AND Bi are both 1.
  Gi = Ai Bi
    Column i will propagate a carry in to the carry out if Ai OR Bi is 1.
  Pi = Ai + Bi
    The carry out of column i (Ci) is:
  Ci = Ai Bi + (Ai + Bi )Ci-1 = Gi + Pi Ci-1
Carry-Lookahead Adder

## Slide 8
Step 1: Compute Gi and Pi for all columns
Step 2: Compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate block
Carry-Lookahead Addition

## Slide 9
Computes carry in (Ci-1) for each column, then computes sum:
Si = (Ai Å Bi) Å Ci
Computes G and P for 1-, 2-, 4-, 8-bit blocks, etc. until all Gi (carry in) known
log2N stages
Prefix Adder

## Slide 10
Carry in either generated in a column or propagated from a previous column.
Column -1 holds Cin, so
  G-1 = Cin, P-1 = 0
Carry in to column i = carry out of column i-1:
  Ci-1 = Gi-1:-1
Gi-1:-1: generate signal spanning columns i-1 to -1
Sum equation:
  Si = (Ai Å Bi) Å Gi-1:-1
Goal: Quickly compute G0:-1, G1:-1, G2:-1, G3:-1, G4:-1, G5:-1, … (called prefixes)
Prefix Adder

## Slide 11
Generate and propagate signals for a block spanning bits i:j:
  Gi:j = Gi:k + Pi:k Gk-1:j
  Pi:j = Pi:kPk-1:j
In words:
  Generate: block i:j will generate a carry if:
    upper part (i:k) generates a carry or
    upper part propagates a carry generated in lower part (k-1:j)
  Propagate: block i:j will propagate a carry if both the upper and lower parts propagate the carry
Prefix Adder

## Slide 12
Prefix Adder Schematic
Sklansky adder

## Slide 13
tPA = tpg + log2N(tpg_prefix ) + tXOR
  tpg: delay to produce Pi Gi (AND or OR gate)
  tpg_prefix: delay of black prefix cell (AND-OR gate)
Prefix Adder Delay

## Slide 14
Compare delay of: 32-bit ripple-carry, carry-lookahead, and prefix adders
CLA has 4-bit blocks
2-input gate delay = 100 ps; full adder delay = 300 ps
tripple = NtFA = 32(300 ps)
= 9.6 ns
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
= [100 + 600 + (7)200 + 4(300)] ps
= 3.3 ns
tPA = tpg + log2N(tpg_prefix ) + tXOR
= [100 + log232(200) + 100] ps
= 1.2 ns
Adder Delay Comparisons

## Slide 15
Subtracter

## Slide 16
Comparator: Equality

## Slide 17
Logical shifter: shifts value to left or right and fills empty spaces with 0’s
  Ex: 11001 >> 2 =
  Ex: 11001 << 2 =
Arithmetic shifter: same as logical shifter, but on right shift, fills empty spaces with the old most significant bit (msb).
  Ex: 11001 >>> 2 =
  Ex: 11001 <<< 2 =
Rotator: rotates bits in a circle, such that bits shifted off one end are shifted into the other end
  Ex: 11001 ROR 2 =
  Ex: 11001 ROL 2 =
Shifters
<<< is not an Java operator
And >>> works differently in Java

## Slide 18
Logical shifter:
  Ex: 11001 >> 2 = 00110
  Ex: 11001 << 2 = 00100
Arithmetic shifter:
  Ex: 11001 >>> 2 = 11110
  Ex: 11001 <<< 2 = 00100
Rotator:
  Ex: 11001 ROR 2 = 01110
  Ex: 11001 ROL 2 = 00111
Shifters

## Slide 19
Shifter Design
shamt determines the amount of the shift

## Slide 20
A << N = A × 2N
  Example: 00001 << 2 = 00100 (1 × 22 = 4)
  Example: 11101 << 2 = 10100 (-3 × 22 = -12)
A >>> N = A ÷ 2N
  Example: 01000 >>> 2 = 00010 (8 ÷ 22 = 2)
  Example: 10000 >>> 2 = 11100 (-16 ÷ 22 = -4)
Shifters as Multipliers, Dividers

## Slide 21
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result
Multipliers

## Slide 22
4 x 4 Multiplier
This may be called
“grid multiplication” in elementary schools

## Slide 23
4 x 4 Divider
A/B = Q + R/B
Algorithm:
R’ = 0
for i = N-1 to 0
R = {R’ << 1. Ai}
D = R - B
if D < 0, Qi=0, R’=R
else Qi=1, R’=D
R’=R

## Slide 24
Numbers we can represent using binary representations
  Positive numbers
    Unsigned binary
  Negative numbers
    Two’s complement
    Sign/magnitude numbers
What about fractions?
Number Systems

## Slide 25
Two common notations:
  Fixed-point: binary point fixed
  Floating-point: binary point floats to the right of the most significant 1
Numbers with Fractions

## Slide 26
6.75 using 4 integer bits and 4 fraction bits:
  Binary point is implied
  The number of integer and fraction bits must be agreed upon beforehand
Fixed-Point Numbers

## Slide 27
Representations:
  Sign/magnitude
  Two’s complement
Example: Represent -7.510 using 4 integer and 4 fraction bits
  Sign/magnitude:
  11111000
  Two’s complement:
  1. +7.5: 01111000
  2. Invert bits: 10000111
  3. Add 1 to lsb: + 1
  10001000
Signed Fixed-Point Numbers
Sensors often use fixed point numbers

## Slide 28
Binary point floats to the right of the most significant 1
Similar to decimal scientific notation
For example, write 27310 in scientific notation:
  273 = 2.73 × 102
In general, a number is written in scientific notation as:
± M × BE
  M = mantissa
  B = base
  E = exponent
  In the example, M = 2.73, B = 10, and E = 2
Floating-Point Numbers

## Slide 29
Example: represent the value 22810 using a 32-bit floating point representation
We show three versions –final version is called the IEEE 754 floating-point standard
Floating-Point Numbers

## Slide 30
Convert decimal to binary (don’t reverse steps 1 & 2!):
  22810 = 111001002
Write the number in “binary scientific notation”:
  111001002 = 1.110012 × 27
Fill in each field of the 32-bit floating point number:
  The sign bit is positive (0)
  The 8 exponent bits represent the value 7
  The remaining 23 bits are the mantissa
Floating-Point Representation 1

## Slide 31
First bit of the mantissa is always 1:
  22810 = 111001002 = 1.11001 × 27
So, no need to store it: implicit leading 1
Store just fraction bits in 23-bit field
Floating-Point Representation 2

## Slide 32
Biased exponent: bias = 127 (011111112)
  Biased exponent = bias + exponent
  Exponent of 7 is stored as:
  127 + 7 = 134 = 0x100001102
The IEEE 754 32-bit floating-point representation of 22810
in hexadecimal: 0x43640000
Floating-Point Representation 3

## Slide 33
Write -58.2510 in floating point (IEEE 754)
Convert decimal to binary:
  58.2510 = 111010.012
Write in binary scientific notation:
1.1101001 × 25
Fill in fields:
  Sign bit: 1 (negative)
  8 exponent bits: (127 + 5) = 132 = 100001002
  23 fraction bits: 110 1001 0000 0000 0000 0000
in hexadecimal: 0xC2690000
Now try 7.7
Floating-Point Example

## Slide 34
Number | Sign | Exponent | Fraction
0 | X | 00000000 | 00000000000000000000000
∞ | 0 | 11111111 | 00000000000000000000000
- ∞ | 1 | 11111111 | 00000000000000000000000
NaN | X | 11111111 | non-zero
Floating-Point: Special Cases
When the exponent field is 0000000, the floating point number is unnormalized.
Take a look at http://www.cs.unca.edu/brock/classes/Fall2013/csci255/notes/Arithmetic.ods

## Slide 35
Single-Precision:
  32-bit
  1 sign bit, 8 exponent bits, 23 fraction bits
  bias = 127
Double-Precision:
  64-bit
  1 sign bit, 11 exponent bits, 52 fraction bits
  bias = 1023
Floating-Point Precision

## Slide 36
Overflow: number too large to be represented
Underflow: number too small to be represented
Rounding modes:
  Down
  Up
  Toward zero
  To nearest
Example: round 1.100101 (1.578125) to only 3 fraction bits
  Down: 1.100
  Up: 1.101
  Toward zero: 1.100
  To nearest: 1.101 (1.625 is closer to 1.578125 than 1.5 is)
Floating-Point: Rounding

## Slide 37
Extract exponent and fraction bits
Prepend leading 1 to form mantissa
Compare exponents
Shift smaller mantissa if necessary
Add mantissas
Normalize mantissa and adjust exponent if necessary
Round result
Assemble exponent and fraction back into floating-point format
Floating-Point Addition

## Slide 38
1. Extract exponent and fraction bits
For first number (N1): S = 0, E = 127, F = .1
For second number (N2): S = 0, E = 128, F = .101
2. Prepend leading 1 to form mantissa
N1: 1.1
N2: 1.101
Floating-Point Addition Example

## Slide 39
3. Compare exponents
127 – 128 = -1, so shift N1 right by 1 bit
4. Shift smaller mantissa if necessary
shift N1’s mantissa: 1.1 >> 1 = 0.11 (× 21)
5. Add mantissas
0.11 × 21
+ 1.101 × 21
10.011 × 21
Floating-Point Addition Example

## Slide 40
6. Normalize mantissa and adjust exponent if necessary
10.011 × 21 = 1.0011 × 22
7. Round result
No need (fits in 23 bits)
8. Assemble exponent and fraction back into floating-point format
S = 0, E = 2 + 127 = 129 = 100000012, F = 001100..
in hexadecimal: 0x40980000
Floating Point Addition Example

## Slide 41
Increments on each clock edge
Used to cycle through numbers. For example,
  000, 001, 010, 011, 100, 101, 110, 111, 000, 001…
Example uses:
  Digital clock displays
  Program counter: keeps track of current instruction executing
Counters

## Slide 42
Implementation:
Shift a new bit in on each clock edge
Shift a bit out on each clock edge
Serial-to-parallel converter: converts serial input (Sin) to parallel output (Q0:N-1)
Shift Registers
Symbol:

## Slide 43
When Load = 1, acts as a normal N-bit register
When Load = 0, acts as a shift register
Now can act as a serial-to-parallel converter (Sin to Q0:N-1) or a parallel-to-serial converter (D0:N-1 to Sout)
Shift Register with Parallel Load

## Slide 44
Efficiently store large amounts of data
3 common types:
  Dynamic random access memory (DRAM)
  Static random access memory (SRAM)
  Read only memory (ROM)
M-bit data value read/ written at each unique N-bit address
Memory Arrays

## Slide 45
2-dimensional array of bit cells
Each bit cell stores one bit
N address bits and M data bits:
  2N rows and M columns
  Depth: number of rows (number of words)
  Width: number of columns (size of word)
  Array size: depth × width = 2N × M
Memory Arrays

## Slide 46
22 × 3-bit array
Number of words: 4
Word size: 3-bits
For example, the 3-bit word stored at address 10 is 100
Memory Array Example

## Slide 47
Memory Arrays

## Slide 48
0
1
Z
Z
Memory Array Bit Cells

## Slide 49
Wordline:
  like an enable
  single row in memory array read/written
  corresponds to unique address
  only one wordline HIGH at once
Memory Array

## Slide 50
Random access memory (RAM): volatile
Read only memory (ROM): nonvolatile
Types of Memory

## Slide 51
Volatile: loses its data when power off
Read and written quickly
Main memory in your computer is RAM (DRAM)
Historically called random access memory because any data word accessed as easily as any other (in contrast to sequential access memories such as a tape recorder)
RAM: Random Access Memory

## Slide 52
Nonvolatile: retains data when power off
Read quickly, but writing is impossible or slow
Flash memory in cameras, thumb drives, and digital cameras are all ROMs
  Historically called read only memory because ROMs were written at manufacturing time or by burning fuses. Once ROM was configured, it could not be written again. This is no longer the case for Flash memory and other types of ROMs.
ROM: Read Only Memory

## Slide 53
DRAM (Dynamic random access memory)
SRAM (Static random access memory)
Differ in how they store data:
  DRAM uses a capacitor
  SRAM uses cross-coupled inverters
Types of RAM

## Slide 54
Invented DRAM in 1966 at IBM
Others were skeptical that the idea would work
By the mid-1970’s DRAM in virtually all computers
Robert Dennard, 1932 -

## Slide 55
Data bits stored on capacitor
Dynamic because the value needs to be refreshed (rewritten) periodically and after read:
  Charge leakage from the capacitor degrades the value
  Reading destroys the stored value
DRAM

## Slide 56
DRAM

## Slide 57
SRAM

## Slide 58
DRAM bit cell:
SRAM bit cell:
Memory Arrays Review

## Slide 59
Developed memories and high speed circuits at Toshiba, 1971-1994
Invented Flash memory as an unauthorized project pursued during nights and weekends in the late 1970’s
The process of erasing the memory reminded him of the flash of a camera
Toshiba slow to commercialize the idea; Intel was first to market in 1988
Flash has grown into a $25 billion per year market
Fujio Masuoka, 1944 -

## Slide 60
ROM Storage

## Slide 61
Data2 = A1 Å A0
Data1 = A1 + A0
Data0 = A1A0
ROM Logic

## Slide 62
Implement the following logic functions using a 22 × 3-bit ROM:
  X = AB
  Y = A + B
  Z = A B
Example: Logic with ROMs

## Slide 63
Data2 = A1 Å A0
Data1 = A1 + A0
Data0 = A1A0
Logic with Any Memory Array

## Slide 64
Implement the following logic functions using a 22 × 3-bit memory array:
  X = AB
  Y = A + B
  Z = A B
Logic with Memory Arrays

## Slide 65
Called lookup tables (LUTs): look up output at each input combination (address)
Logic with Memory Arrays

## Slide 66
Port: address/data pair
3-ported memory
  2 read ports (A1/RD1, A2/RD2)
  1 write port (A3/WD3, WE3 enables writing)
Register file: small multi-ported memory
Multi-ported Memories

## Slide 67
// 256 x 3 memory module with one read/write port
module dmem( input logic clk, we,
input logic [7:0] a,
input logic [2:0] wd,
output logic [2:0] rd);
logic [2:0] RAM[255:0];
assign rd = RAM[a];
always @(posedge clk)
if (we)
RAM[a] <= wd;
endmodule
SystemVerilog Memory Arrays

## Slide 68
PLAs (Programmable logic arrays)
  AND array followed by OR array
  Combinational logic only
  Fixed internal connections
FPGAs (Field programmable gate arrays)
  Array of Logic Elements (LEs)
  Combinational and sequential logic
  Programmable internal connections
Logic Arrays

## Slide 69
X = ABC + ABC
Y = AB
PLAs

## Slide 70
PLAs: Dot Notation

## Slide 71
Composed of:
  LEs (Logic elements): perform logic
  IOEs (Input/output elements): interface with outside world
  Programmable interconnection: connect LEs and IOEs
  Some FPGAs include other building blocks such as multipliers and RAMs
FPGA: Field Programmable Gate Array

## Slide 72
General FPGA Layout

## Slide 73
Composed of:
  LUTs (lookup tables): perform combinational logic
  Flip-flops: perform sequential logic
  Multiplexers: connect LUTs and flip-flops
LE: Logic Element

## Slide 74
Altera Cyclone IV LE

## Slide 75
The Altera Cyclone IV LE has:
  1 four-input LUT
  1 registered output
  1 combinational output
Altera Cyclone IV LE

## Slide 76
Show how to configure a Cyclone IV LE to perform the following functions:
  X = ABC + ABC
  Y = AB
LE Configuration Example

## Slide 77
Using a CAD tool (such as Altera’s Quartus II)
  Enter the design using schematic entry or an HDL
  Simulate the design
  Synthesize design and map it onto FPGA
  Download the configuration onto the FPGA
  Test the design
FPGA Design Flow