## Slide 1: IMU Guidance
Servoblaster
Code for the IMU
Going mobile

## Slide 2: Build the Basic Bot
Build your bot using the parallax chassis
  Use a battery pack that holds 6 AA batteries
  Mount your breadboard so that it’s center groove is aligned with the plane of symmetry of the chassis
  Instructions for mounting the servos to the chassis can be found on page 73 of Robotics with the Boe-Bot
  Mount your T-cobbler on your breadboard and connect it to the Pi
    Judicious (i.e., using small amounts) apply double-sticky-back tape to secure your breadboard and the Pi to the chassis

## Slide 3: Parallax Servo Connections
Servo Connector:
Black – ground
Red – power
White – signal
Image credit: http://www.parallax.com/

## Slide 4: Servoblaster Setup
Download Servoblaster from GitHub per instructions in your HW
Install “user space” daemon
  Edit init-script to set idle-timeout if desired
    Edit /etc/init.d/servoblaster if already installed
  Command: sudo make install
    Causes code to always initiate at system start-up
Run program to view parameter
  Command: servod

## Slide 5: Running Servoblaster
Servoblaster can run 8 servos at once
  Note pin assignments in output of servod
  For this effort, I suggest using GPIO17 and GPIO18
Connect your servos
  Connect GPIO17 to the white wire in one servo header
  Connect GPIO18 to the white wire in the other servo header
      Connect the black wires in the servo headers to ground
      Connect the red wires in the servo headers a 5V supply
    Run the servos using servoblaster
      E.G. command: echo 1=120 > /dev/servoblaster
Servod Pin Numbers:

## Slide 6: Mount the MPU-6050 on Your Breadboard
Connecting the MPU to the Pi
  MPU6050 Pi Pin ID
  Pin ID VDD --> 3.3V on Pi
  GND --> GND on Pi SCL --> SCL on Pi
  SDA --> SDA on Pi
  XDA XCL ADO --> GND on Pi INT

## Slide 7: Checkout the IMU
Try the following to assure that your IMU is working:
  sudo i2cdetect -y 1
  ./demo_dmp
  ./demo_3d

## Slide 8: Programming the IMU
Object: A program to travel at a specific heading
  Combine demo_dmp.cpp and our earlier line following code to program a bot that travels forward at a pre-defined angular orientation
Approach:
  Edit and re-purpose loop() in demo_dmp.cpp to read the IMU
    Use just the yaw values (rotation about z)
    Add a return value to test for a good read
    Could adjust FIFO sample rate---this is done in the Makefile
    Recognize gyro drift when possible!
    Recognize occasional 180 degree angle flip.

## Slide 9: Controlling the Servos
#include <stdio.h>
#include <stdlib.h>
int main(void) {
FILE *fp;
fp = fopen("/dev/servoblaster", "w");
if (fp == NULL) {
printf("Unable to open file\n");
exit(0);
}
fprintf(fp, "2=200\n");
fflush(fp);
fclose(fp);
return 0;
}

## Slide 10: Putting It All Together
IMUfollowing.cpp
Makefile
Problems:
  Gryo drift
  Servo control
  Never properly tested

## Slide 11: Battery Power
The Pi draws a lot of current
Proposed hardware:
  (6) AAs (nominally 8 V)
  (2) 5 Volt regulators
  (4) capacitors
Separate Pi from the servos
  Output of one regulator is 5V input to the Pi
  Output of one regulator is 5V power for servos
  Input to both regulators is the battery pack
  Put capacitors on both regulator inputs and outputs
  Everything on a common ground

## Slide 12: Two power supplies with a common ground