## Slide 1: Intro to Robot Movement
Topics:
  DC motors
  Servos
  Line following

## Slide 2: Many ways to move
Focus on wheeled movement

## Slide 3: Alternative drive-trains
Demos
  Mecanum demo
  UNCA demo
Mecanum
wheel
Omni
wheel
Image credit: http://members.toast.net/joerger/oldarchive.html

## Slide 4: Making wheels move (using servos)
Image credit: http://induino.blogspot.com

## Slide 5: Topic 1: DC Motor
Electromagnetism: A changing magnetic field makes an electric field. A changing electric field makes a magnetic field.
How it works
Image credit: http://en.wikipedia.org

## Slide 6: Topic 2: Servos
Servo motors can also be retrofitted to provide continuous rotation:
  Remove mechanical limit (revert back to DC motor shaft).
  Remove pot position sensor (no need to know position) and replace it with 2 equal-valued resistors with a combined resistance equivalent to that of the pot. Makes the servo “think” it is in the 90 deg position.
Image credit: http://www.engineersgarage.com
Not always
necessary

## Slide 7: Servo control
An external controller (such as the Arduino) tells the servo where to go with a signal know as pulse proportional modulation (PPM) or pulse code modulation (which is often confused with pulse width modulation, PWM).
PPM uses 1 to 2ms out of a 20ms time period to encode information.
Image credit: http://www.engineersgarage.com

## Slide 8: PPM
Each pulse is from 1300 to 1700 microsec (μs) in duration
The pulses repeat about 50 times each second---once every 20 millisec
Image credit: http://www.elprocus.com/servo-motor/
20 ms

## Slide 9: Continuous rotation servo
The amount of power applied to the motor is proportional to the distance to be traveled.
If the shaft needs to turn a large distance, the motor runs at full speed.
If it needs to turn a small amount, the motor runs at a slower speed.
and speed

## Slide 10: Analog vs digital servos
Advantages:
  Higher and more consistent torque throughout the servo travel
  Constant holding power when stationary and less deadband
  Faster control response - increased acceleration
Disadvantages:
  Higher costs
  More power consumption
Image credit: http://www.sailservo.co.uk/anvdig.html

## Slide 11: Parallax Servo Connections
Servo Connector:
Black – ground
Red – power
White – signal
Image credit: http://www.parallax.com/

## Slide 12: Calibration Program
#include <Servo.h>
Servo myServo;
void setup() {
myServo.attach(9);
myServo.writeMicroseconds(1500); // Stop
}
void loop() { }
The parallax servos are modified servos with the potentiometer intact.
The potentiometer (a.k.a., pot) should be adjusted to make the servo think that it is at the 90 degree mark. Do that now.
Servo library

## Slide 13: In-Class Activity 1
Read and work activity 6 in Chapter 2 of Parallax’s Robotics with the Board of Education Shield for Arduino. The activity makes reference to the “BOE Shield,” a piece of hardware designed by Parallax to interface with the Arduino. The shield contains a breadboard as well as a few switches and connectors that we don’t have, but not to worry. The Arduino programs and the information about the Parallax servos are correct for our setup.
Complete the assembly of your boe-bot chassis before beginning activity 6. The completed chassis should include both servos, the arduino, and the breadboard. For power, you can leave your robot tethered to the USB cable or use a battery pack.

## Slide 14: Topic 3: Line Following
Pololu QTR-8A Reflectance Sensor Array

## Slide 15: QTI sensor
The QTI is a reflective object sensor. There’s an infrared LED behind its clear window and an infrared phototransistor behind its black window.
When the infrared light emitted by the LED reflects off a surface and returns to the black window, it strikes the infrared phototransistor’s base, causing it to conduct current.
The more infrared incident on the phototransistor’s base, the more current it conducts.
Image credit: http://www.parallax.com/
Connect to power
Connect to ground
Connect to digital pin

## Slide 16: Using a sensor array
Control the servos based on the sensor readings
The more sensors the more accurate the control
Image: http://hirobotblog.blogspot.com/2012/08/algorithms-2-bit-of-maths.html

## Slide 17: Line following with one sensor?
try to follow the edge of the line
Image credit: http://www.inpharmix.com/jps/PID_Controller_For_Lego_Mindstorms_Robots.html

## Slide 18: Code (missing two functions)
#include <Servo.h> // Include servo library
Servo servoLeft; Servo servoRight; // Declare left and right servo objects
//Parameters
int target = 210; // target sensor reading
int maxSpeed = 100; // control forward speed
void setup() { // initialization method
Serial.begin(9600);
servoLeft.attach(12); // Attach left signal to pin 13
servoRight.attach(3); // Attach right signal to pin 12
}
void loop() { // main loop auto-repeats
int light = (int) rcTime(9); // Read QTI sensor
float error = light - target; // Difference between target &current reading
int speedLeft, speedRight; // Declare speed variables
if (error > 0.0) { // over only black?
speedLeft = -maxSpeed; // Slow down left wheel
speedRight = maxSpeed; // Full speed right wheel
} else { // over only white?
speedRight = -maxSpeed; // Slow down right wheel
speedLeft = maxSpeed; // Full speed left wheel
}
maneuver(speedLeft, speedRight, 20); // Set wheel speeds
}

## Slide 19: rcTime() function
// rcTime function measures decay at pin
long rcTime(int pin) {
pinMode(pin, OUTPUT); // Charge capacitor
digitalWrite(pin, HIGH); // ..by setting pin ouput-high
delay(5); // ..for 5 ms
pinMode(pin, INPUT); // Set pin to input
digitalWrite(pin, LOW); // ..with no pullup
long time = micros(); // Mark the time
while(digitalRead(pin)); // Wait for voltage < threshold
time = micros() - time; // Calculate decay time
return time; // Returns decay time
}

## Slide 20: maneuver() function
// maneuver function
void maneuver(int speedLeft, int speedRight, int msTime) {
servoLeft.writeMicroseconds(1500 + speedLeft); // Set left servo speed
servoRight.writeMicroseconds(1500 - speedRight); // Set right servo speed
if(msTime==-1) { // if msTime = -1
servoLeft.detach(); // Stop servo signals
servoRight.detach();
}
delay(msTime); // Delay for msTime
}

## Slide 21: Proportional line following
In proportional line following the turn varies smoothly between two limits
If the light sensor reading indicates close to the line then do a small turn
If far from the line then do a big turn
Proportional means there is a linear relationship between the sensor reading and robot movement
Image credit: http://www.inpharmix.com/jps/PID_Controller_For_Lego_Mindstorms_Robots.html

## Slide 22: Code: loop() only
float kp = 0.5;
void loop() { // main loop auto-repeats
int light = (int)rcTime(9);
float error = light - target;
int speedLeft, speedRight; // Declare speed variables
if (error > 0.0) { // on black only ?
speedLeft = int(maxSpeed - (error * kp)); // proportion adjust
speedLeft = constrain(speedLeft, -maxSpeed, maxSpeed); // scale left wheel speed
speedRight = maxSpeed; // Full speed right wheel
} else { // on white only ?
speedRight = int(maxSpeed + (error * kp)); // proportion adjust
speedRight = constrain(speedRight, -maxSpeed, maxSpeed); // scale right wheel speed
speedLeft = maxSpeed; // Full speed left wheel
}
maneuver(speedLeft, speedRight, 20); // Set wheel speeds
}

## Slide 23: PID control
KP, KI, and KD are tunable constants (i.e., weights)
(KP e) proportional to the current error—the basis of the previous algorithm
(KI ∫e) —the integral is the running sum of the error
  integral = integral + error*(dT)
(KD de/dt) —the derivative is the change in the error between two consecutive sensor readings
  derivative = ((the current error) - (the previous error)) /(dT)
movement = Kp*(error) + Ki*(integral) + Kd*(derivative)

## Slide 24: Code: part of loop()
void loop() { // Main loop auto-repeats
int light = (int)rcTime(9); // read sensor
float error = light - target; // proportional term
int delta = error - prevError; // derivative term
integral = integral + error; // integral term
prevError = error;
float correction = (integralMemory * integral * ki) + (error * kp) + (delta * kd);
int speedLeft, speedRight; // Declare speed variables
if (correction > 0.0) { // over black only?
speedLeft = int(maxSpeed - correction);
speedLeft = constrain(speedLeft, -maxSpeed, maxSpeed);
speedRight = maxSpeed;
} else { // over white only?
speedRight = int(maxSpeed + correction);
speedRight = constrain(speedRight, -maxSpeed, maxSpeed);
speedLeft = maxSpeed;
}
…
Link to the full program

## Slide 25: Two sensors?
place them on either side of the line
OR
Image credit: http://kile.stravaganza.org/project/lego-robot-line-follower

## Slide 26: Two sensor proportional line following
Image credit: http://www.seattlerobotics.org/encoder/200011/Line%20Following.htm
Image credit: http://www.inpharmix.com/jps/PID_Controller_For_Lego_Mindstorms_Robots.html
Control based on the difference between the sensors readings:
  Negate left sensor reading
  Sum the right and left sensor readings
  Move based on the difference

## Slide 27: In-Class Activity 2
Create a two-sensor line-following robot and compete in the in-class competition.
Members of the winning team will each receive 5 extra credit pts.